## Slide 1: MODIS AOD retrieval: Dark Target merged with Deep Blue
3 · Remote sensing of aerosols and radiation
MODIS L1B radiances
Terra / Aqua, 0.41–2.13 µm
Pre-processing
Mask cloud, snow, water · Rayleigh correction
Dark Target
Dark, vegetated land
Surface from 2.13 µm band (VIS/SWIR ratio)
LUT: fine + coarse models
Deep Blue
Bright land: desert, city, dry crop
Surface from 0.41/0.49 µm library
LUT: dust / smoke models
Merge by NDVI
NDVI > 0.3
use Dark Target
NDVI 0.2–0.3
mean of both
NDVI < 0.2
use Deep Blue
Combined DT–DB AOD at 0.55 µm, 10 km
MOD04 / MYD04 · EE ±(0.05 + 0.15τ)
Levy et al., 2013; Hsu et al., 2013; Sayer et al., 2014
Notes: This flowchart shows how the standard MODIS aerosol product combines the two land algorithms. Both start from the same MODIS Level 1B radiances from Terra and Aqua, covering 0.41 to 2.13 micrometres. Pixels affected by cloud, snow and water are masked, and Rayleigh scattering by air molecules is removed. The retrieval then follows two branches. Dark Target, described by Levy and colleagues, works over dark vegetated land: it estimates visible surface reflectance from the 2.13 micrometre band, where aerosol is almost transparent, and inverts look-up tables built from fine and coarse aerosol models. Deep Blue, described by Hsu and colleagues, works over bright surfaces such as deserts, cities and dry cropland: at 0.41 and 0.49 micrometres these surfaces are dark, so surface reflectance is taken from a pre-computed database, and dust or smoke models are used for the inversion. In Collection 6 the two are merged into a single combined product using NDVI, as described by Sayer and colleagues, 2014. Where NDVI is above 0.3 the Dark Target value is used; where NDVI is below 0.2 the Deep Blue value is used; between 0.2 and 0.3 the mean of both is used when both have good quality, otherwise the one with better quality. The output is the combined Dark Target–Deep Blue AOD at 0.55 micrometres and 10 kilometres resolution in the MOD04 and MYD04 products, validated against AERONET with an expected error over land of plus or minus 0.05 plus 15 percent of AOD. This merging gives near-complete coverage over India, including the bright dry-season croplands of the Indo-Gangetic Plain where Dark Target alone fails.