## Slide 1: Multimodal image fusion for UAV-based disease severity assessment: data, pixel, feature and decision/model level
Concepts, ML and DL methods, evidence from the literature, and a step-by-step workflow for white rust (Albugo candida) in mustard · MuDAS-AI · Animesh Panda, ICAR-IARI
Notes: Purpose: one place for every fusion concept needed in the thesis. Each content slide ends with an 'In MuDAS-AI' strip that links the concept to the study, and a reference line. Full references are on the last four slides.

## Slide 2: The study and its fusion objectives
CONTEXT
In MuDAS-AI: every fusion option in this deck is judged by one question: does it improve white rust severity classification on unseen plots, at acceptable cost and complexity?
Study design as planned for MuDAS-AI; fusion definitions: Hall & Llinas (1997); Lahat et al. (2015).
Field data
Trial: IARI, 48 plots (12 healthy controls, 36 inoculated), 4 flight dates
Sensors: RGB, multispectral (MicaSense, 5 bands), hyperspectral (VNIR), thermal
Labels: plot disease index (DI) → 6 ordered classes (0 healthy … 5 very high)
Validation: IARI held-out plots → IIRMR Bharatpur → farmers' fields
Complementary: glasshouse pot experiment (leaf/plant scale)
Fusion objectives
O1: identify disease-specific features of each sensor (single-sensor level)
O2: build the best single-sensor model (baseline)
O3: fuse sensors and compare fusion levels: data/pixel, feature (ML and DL), decision/model
O4: find the smallest sensor set that is accurate enough (cost)
O5: produce a validated severity map and spray zones

## Slide 3: Why fuse? Each sensor measures a different physical property
CONCEPT · COMPLEMENTARITY
In MuDAS-AI: fusion is justified only if the sensors carry complementary information about white rust; prove this with low cross-sensor correlation and an ablation table.
Mahlein (2016); Zarco-Tejada et al. (2018); Maimaitijiang et al. (2020); Baltrušaitis et al. (2019) definition of modality.
Sensor | Physical principle | Typical UAV GSD | White rust symptom it can capture
RGB | Reflected visible light, 3 broad bands, very high spatial detail | ≈ 1 cm | Texture: white pustules, chlorotic spots, stagheads, leaf distortion
Multispectral | Reflected light in 5 broad bands incl. red edge and NIR | ≈ 3–5 cm | Canopy vigour and chlorophyll loss (NDVI, NDRE, CIre)
Hyperspectral | Spectroscopy: ~100+ narrow contiguous bands | ≈ 2–5 cm | Pigments, red-edge shift, water bands, subtle early changes
Thermal | Emitted long-wave radiation (energy balance), not reflection | ≈ 5–10 cm | Reduced transpiration → warmer canopy (CTD, NRCT)
Structure (from RGB) | Photogrammetric 3-D surface (DSM − DTM) | ≈ 1–2 cm | Stunting, staghead deformation, canopy height and cover
A modality is defined by its sensing principle, not by the file format: like MRI, CT and PET in medicine, all four are images, yet they measure different properties.

## Slide 4: Fusion levels: a taxonomy
CONCEPT · LEVELS
In MuDAS-AI: the thesis compares Level 2 (feature fusion, ML and DL) and Level 3 (decision fusion); Levels 0–1 are prerequisites or optional enhancements.
Pohl & Van Genderen (1998); Hall & Llinas (1997); Castanedo (2013); Ramachandram & Taylor (2017); Baltrušaitis et al. (2019).
L0 Data level
L1 Pixel level
L2 Feature level
L3 Decision / model level
Hybrid
Level | What is combined | Output | Typical methods
L0 Data (signal) | Raw/calibrated measurements put on a common geometry and radiometry | Co-registered, harmonised layer stack | Calibration, co-registration, resampling, stacking
L1 Pixel | Pixel values of co-registered images | A fused image, or per-pixel joint vectors | Pansharpening (CS, MRA), HS–MS fusion, IR–visible fusion, early-fusion CNN
L2 Feature | Descriptors extracted separately from each sensor | Joint feature vector / representation | Concatenation + selection, PCA/PLS/CCA, multiple kernels, multi-branch DL
L3 Decision / model | Outputs of separate sensor-specific models | Combined class / probability | Voting, weighted averaging, stacking, Dempster–Shafer, DL late fusion
Hybrid | More than one level | Combined | Feature fusion within groups + decision fusion across; multi-stage DL
Notes: 'Data level' and 'pixel level' are often used as synonyms (Pohl & Van Genderen, 1998, use pixel / feature / decision). Here L0 is used for the geometric and radiometric harmonisation that every higher level needs, and L1 for actually combining pixel values.

## Slide 5: Terminology: the same idea has different names
CONCEPT · TERMS
In MuDAS-AI: define the terms once in the Methods chapter (use the left column) to avoid reviewer confusion, especially between 'model-level' and 'decision-level'.
Pohl & Van Genderen (1998); Snoek et al. (2005); Ramachandram & Taylor (2017); Baltrušaitis et al. (2019); Hong et al. (2021).
Term used here | Synonyms in the literature | Note
Data-level fusion | Signal-level, low-level, raw-data fusion | Sometimes includes pixel-level fusion
Pixel-level fusion | Image fusion, early fusion (in DL), input-level fusion | Requires accurate co-registration and a common grid
Feature-level fusion | Intermediate fusion, mid-level fusion, representation fusion | In DL: fusion of learned feature maps or embeddings
Decision-level fusion | Late fusion, classifier fusion, ensemble of sensor models | Combines predictions, not features
Model-level fusion | Used in two ways: (a) = decision/late fusion; (b) a joint model that fuses inside its architecture | State which meaning you use
Joint vs coordinated representation | Baltrušaitis et al. (2019) | Joint: one shared space; coordinated: separate spaces linked by constraints (e.g. CCA)

## Slide 6: Preconditions: what must be true before any fusion works
CONCEPT · REQUIREMENTS
In MuDAS-AI: these six conditions become the checklist for every flight date before features are extracted.
Zitová & Flusser (2003); Pohl & Van Genderen (1998); Varma & Simon (2006); Roberts et al. (2017).
1. Same object, same time
All sensors flown on the same day, in a fixed time window (e.g. ±1.5 h of solar noon)
2. Geometric agreement
Co-registration error well below one pixel of the coarsest sensor used
3. Radiometric consistency
Reflectance (RGB/MS/HS) and °C (thermal) calibrated per flight
4. Common support
Same canopy mask and plot inset for all sensors
5. Matched labels
DI scored on the flight day, on the same plot area the sensors see
6. Leak-free evaluation
Any step that uses labels runs inside plot-grouped training folds

## Slide 7: Step 1 · Multi-sensor flight planning
ACQUISITION
In MuDAS-AI: fix one flight plan per sensor and reuse it on all 4 dates; record actual heights, times and weather in the flight log.
Flight practice: Su et al. (2018); Maimaitijiang et al. (2020); Guo et al. (2021); Liu et al. (2024). GSD = pixel pitch × height / focal length.
Plan
Same day, all sensors; fixed time window around solar noon (stable sun angle; thermal contrast largest)
Order: thermal and MS/HS close to noon; RGB can be slightly earlier/later
Weather: clear sky or uniform overcast, wind < 3–4 m/s; avoid broken clouds
Overlap: ≈ 80 % forward / 75 % side for photogrammetric sensors; push-broom HS needs straight lines and stable speed
Height: chosen so each sensor resolves the canopy; compute GSD for each camera
Repeat identical plans on every date
Sensor | Example height | GSD (typical) | Note
RGB | 20–30 m | ≈ 0.5–1 cm | Texture, DSM
Multispectral | 20–40 m | ≈ 2–4 cm | DLS + panel
Hyperspectral | 30–50 m | ≈ 2–5 cm | Panels, stable speed
Thermal | 20–40 m | ≈ 3–8 cm | Equilibrated camera
Values are typical ranges; compute your own GSD from the camera specifications and chosen height.

## Slide 8: Step 2 · Ground control and radiometric calibration
ACQUISITION
In MuDAS-AI: the same GCPs (visible in RGB, MS, HS and thermal) are the backbone of co-registration; calibration logs make data from IARI and Bharatpur comparable.
Maimaitijiang et al. (2020) GCPs, sunshine sensor, thermal blackbody & ground targets; Su et al. (2018) panels before/after flight; Jones (2004); Leinonen & Jones (2004).
Ground control
≥ 5 GCPs spread over the field + independent check points
Surveyed with RTK GNSS (cm accuracy)
Thermal-visible targets: materials with strong thermal contrast (e.g. aluminium foil + black panel) so the same point is visible in all sensors
Permanent plot corner markers
Calibration targets
MS/HS: reflectance panels (e.g. dark, grey, bright) imaged before and after each flight
MS: downwelling light sensor
Thermal: reference surfaces measured on the ground with a handheld IR thermometer; air T and RH at flight time
RGB: grey card / colour checker
Radiometric processing
RGB: consistent exposure; colour correction
MS: DN → radiance → reflectance (panel + DLS)
HS: dark current, empirical line with panels, remove noisy/water bands, smoothing
Thermal: raw → °C (radiometric), check against ground targets; derive CTD = Tc − Tair

## Slide 9: Step 3 · Ground truth and metadata, designed for fusion
ACQUISITION
In MuDAS-AI: labels must be at the scale of the fused unit (plot or quadrat); score both leaf surfaces because white rust pustules develop on the abaxial side.
Whetton et al. (2018) visual vs photo assessment; Bohnenkamp et al. (2019) rating by leaf level; McKinney (1923) disease index; Olofsson et al. (2014).
Labels
Plot DI on each flight day: same central area as image analysis (after inset), centre + corners
By leaf layer (upper, middle, lower) and both surfaces
DI = Σ(grade × leaves) / (total leaves × max grade) × 100 → 6 classes
Quadrats (0.5–1 m², RTK-located) for sub-plot / pixel-map validation
Optional physiology: SPAD/Dualex, Fv/Fm, canopy height
Metadata (per flight)
Date, time, sensor, height, speed, overlap
Weather: air T, RH, wind, cloud
Calibration files (panels, DLS, thermal targets)
GCP coordinates; processing software and version
File naming: {site}_{date}_{sensor}_{product}.tif
Data dictionary for every feature column

## Slide 10: L0 · Co-registration: concepts and methods
DATA LEVEL
In MuDAS-AI: thermal ↔ visible is the hardest pair (different physics, lower resolution); use GCPs plus mutual information or edge-based matching for fine alignment.
Zitová & Flusser (2003) survey; Lowe (2004) SIFT; Evangelidis & Psarakis (2008) ECC; Maes et al. (1997) mutual information for multimodal registration; Kerkech et al. (2020a).
Component | Options | Comment
Transformation model | Translation, affine, projective (homography), polynomial, elastic | Orthomosaics on the same GCPs usually need only a small affine/translation correction
Feature-based matching | SIFT / ORB keypoints + RANSAC | Works between similar bands (RGB ↔ MS red/green); weak for thermal
Area / intensity-based | Cross-correlation, ECC, mutual information (MI) | MI handles different modalities because it does not assume equal intensities
Structure-based | Match gradient / edge maps (plot borders, paths, GCP targets) | Robust option for NIR ↔ thermal
Iterative refinement | Repeat keypoint detection and matching | Kerkech et al. (2020a) for visible ↔ infrared UAV images

## Slide 11: L0 · Co-registration workflow and accuracy check
DATA LEVEL
In MuDAS-AI: report co-registration RMSE per sensor and date in the thesis; if thermal error exceeds about half a thermal pixel, use plot-level features rather than pixel fusion.
Zitová & Flusser (2003); Maimaitijiang et al. (2020) GCP-based orthomosaics; Kerkech et al. (2020a).
Orthomosaic each sensor with the same GCPs
Reproject to one CRS
Choose reference sensor (MS)
Fine alignment (MI / edges)
Resample to target grid
Check RMSE on check points
Practical settings
Reference grid: the MS orthomosaic (good geometry, NIR edges)
Fine alignment on plot-border edges / GCP targets
Estimate shift with sub-pixel precision; apply to geotransform
Visual overlay check: NDVI edges vs thermal edges
Accuracy targets
RMSE on independent check points (cm)
Pixel fusion: error ≪ 1 pixel of the coarsest sensor used
Plot-level feature fusion: tolerant if plots are inset (0.4 m) and features are plot means
Document failures (wind, blur) and drop affected tiles

## Slide 12: L0 · Resolution harmonisation, masking and the layer stack
DATA LEVEL
In MuDAS-AI: keep native resolutions for plot-level features (ML); build a common 5 cm stack only for pixel/patch DL experiments.
Pohl & Van Genderen (1998); Bohnenkamp et al. (2019) effect of subsampling; Guo et al. (2021) resolution test; Leinonen & Jones (2004) visible mask for thermal.
Harmonise resolution
Option A: aggregate fine sensors to the coarsest grid by area-weighted averaging (not nearest neighbour)
Option B: keep native grids; extract features per plot/tile covering the same ground area
Option C: super-resolve coarse sensors (pixel-level fusion, L1)
Common masks
Canopy mask (NDVI/ExG + Otsu) from the finest sensor, resampled to others
Shadow mask (low NIR); optional flower mask (mustard yellow)
Thermal: use the visible/NIR mask to keep pure leaf pixels (avoids soil-heated mixed pixels)
Plot inset (e.g. 0.4 m) to remove edges
Layer stack (data cube)
Bands: RGB(3) + MS(5) + HS(n or PCA) + TIR(1) + CHM(1)
Stored as GeoTIFF/COG or xarray with band names
Per-band metadata: units, wavelength, date
Output of L0 = input for L1 (pixel) and for tile-based DL

## Slide 13: L1 · Pixel-level fusion: concept
PIXEL LEVEL
In MuDAS-AI: pixel-level fusion is optional: use it to sharpen thermal or hyperspectral, or to feed an early-fusion CNN; the main analysis can stay at feature level.
Pohl & Van Genderen (1998); Ghassemian (2016); Vivone et al. (2015); Yokoya et al. (2017); Ma et al. (2019).
Two meanings
(a) Image fusion: create one new image that combines the spatial detail of one sensor with the spectral/thermal information of another (e.g. pansharpening)
(b) Pixel stacking: use the co-registered values of all sensors at each pixel as one vector for a classifier (early fusion)
Both need accurate co-registration and a common grid
Method families
Component substitution (CS): IHS, PCA, Gram–Schmidt, Brovey
Multiresolution analysis (MRA): wavelets, Laplacian pyramid, high-pass filtering
Model-based / variational / Bayesian
Unmixing-based (e.g. coupled NMF for HS–MS)
Deep learning (CNN/autoencoder fusion networks)

## Slide 14: L1 · Component substitution vs multiresolution analysis
PIXEL LEVEL
In MuDAS-AI: if you sharpen MS or thermal with RGB detail, prefer MRA or regression-based methods and check that spectral/thermal values are preserved (next slides).
Vivone et al. (2015) critical comparison of pansharpening; Ghassemian (2016); Agam et al. (2007) TsHARP thermal sharpening.
Family | How it works | Strength | Risk
CS: IHS / PCA / Gram–Schmidt | Transform the low-resolution image, replace the intensity / first component with the high-resolution band, invert | Sharp, simple | Spectral distortion if bands differ from the high-resolution band
MRA: wavelet / Laplacian / HPF | Extract high-frequency detail from the high-resolution band and inject it into each low-resolution band | Better spectral fidelity | Possible spatial artefacts
Regression sharpening (e.g. TsHARP) | Fit a relation between coarse thermal and a fine index (e.g. NDVI); predict fine thermal | Physically motivated for thermal | Relation may differ for diseased canopy
MRA detail injection: F_k = M̃_k + g_k · (P − P_L) (M̃: upsampled band k; P: high-resolution band; P_L: its low-pass; g_k: gain)

## Slide 15: L1 · Hyperspectral–multispectral and thermal–visible fusion
PIXEL LEVEL
In MuDAS-AI: HS–RGB fusion could give high-resolution spectral maps for within-plot hotspots; thermal–visible fusion mainly helps visual interpretation; neither replaces calibrated features.
Yokoya et al. (2012) coupled NMF; Yokoya et al. (2017) HS–MS fusion review; Ma et al. (2019) IR–visible fusion survey; Li & Wu (2019) DenseFuse.
Hyperspectral + multispectral / RGB
Goal: high spatial AND high spectral resolution
Unmixing-based: coupled NMF estimates endmembers from HS and abundances from MS, then recombines
Bayesian / sparse / variational methods
DL super-resolution (CNN fusion networks)
Useful when HS is coarser than RGB/MS
Thermal + visible
Goal: one image with thermal targets and visible texture
Methods: MRA, sparse representation, DL (e.g. DenseFuse autoencoder)
Fused images are mostly for visualisation; their pixel values are no longer °C
Quantitative alternative: use the visible mask to select pure leaf thermal pixels (data-level)

## Slide 16: L1 · Quality assessment of fused images
PIXEL LEVEL
In MuDAS-AI: any fused image used for features must pass spectral-fidelity checks (SAM, ERGAS) against the original sensor; otherwise use the original bands.
Wald et al. (1997) protocol; Wang et al. (2004) SSIM; Alparone et al. (2008) QNR; Vivone et al. (2015).
Metric | Measures | Ideal
Wald protocol | Consistency: fused image degraded back to low resolution ≈ original; synthesis at reduced scale | Close agreement
SAM (spectral angle mapper) | Spectral distortion per pixel (angle between spectra) | 0°
ERGAS | Relative global error across bands, scaled by resolution ratio | Low
SSIM | Structural similarity of images | 1
Q2n / Q4 | Joint spectral-spatial quality index | 1
QNR (no reference) | Spectral and spatial distortion without a reference image | 1

## Slide 17: L1 · Pixel-level classification with a stacked cube (ML and DL)
PIXEL LEVEL
In MuDAS-AI: your labels are plot-level, so pixel classifiers need weak supervision (slide 33) or quadrat/pixel annotations; never split pixels of one plot between training and test.
Kerkech et al. (2020a) SegNet on visible/IR; Pan et al. (2021) PSPNet; Roberts et al. (2017) blocked CV; Ronneberger et al. (2015) U-Net; Breiman (2001); Cortes & Vapnik (1995).
ML per pixel
Input: pixel vector [RGB, MS, HS, TIR]
Classifier: RF, SVM, KNN
Needs pixel labels (annotated lesions/healthy tissue)
No spatial context unless texture added
DL per pixel / patch
Patch CNN (centre pixel label) or segmentation (U-Net, SegNet, PSPNet)
Early fusion: stack all channels at input
Learns spatial-spectral patterns
Needs many labelled pixels / masks
Label problem
Plot DI ≠ pixel severity (change of support)
Options: annotate mm-scale RGB of quadrats; weak supervision (MIL, label proportions); unmixing fractions
Split by plot: pixel-level random splits inflate accuracy

## Slide 18: L2 · Feature-level fusion: concept
FEATURE LEVEL
In MuDAS-AI: this is the core of MuDAS-AI (Phases 1–3); it tolerates small misregistration and different resolutions because each sensor is summarised per plot first.
Pohl & Van Genderen (1998); Gómez-Chova et al. (2015); Maimaitijiang et al. (2020); Feng et al. (2022).
Masked images
Features
Scale
Concat
Select
Classify
Advantages
Sensors can have different resolutions
Physically interpretable features (indices, CTD, texture)
Works with few samples when combined with feature selection
Easy ablation: drop one sensor's features
Challenges
High dimensionality (HS) vs few plots → selection needed
Redundancy between sensors (e.g. MS NDRE ≈ HS red edge)
Unequal feature counts per sensor (one sensor can dominate)
Hand-crafted features may miss unknown patterns

## Slide 19: L2 · Feature extraction per sensor
FEATURE LEVEL
In MuDAS-AI: all of these are computed per plot (and per tile for DL) in s05_features.py; percentiles and texture are often more sensitive than plot means.
Maimaitijiang et al. (2020); Liu et al. (2024) percentiles & TTCI; Feng et al. (2022); Zhang et al. (2012); Tian et al. (2021) CWT; Guo et al. (2021); Mahlein et al. (2019).
Sensor | Spectral / radiometric | Spatial / texture | Other
RGB | Chromatic r, g, b; ExG, VARI, GLI | GLCM (contrast, entropy, homogeneity…); pustule-pixel fraction | Canopy height & cover (DSM − DTM)
MS | Bands; NDVI, NDRE, CIre, MTCI, OSAVI, PSRI; percentiles (10–90th) | GLCM on bands | Within-plot SD
HS | Bands; PRI, PSSR, CARI, MCARI, REP; derivatives; continuum removal; CWT; SNV bands | GLCM on PCA components | Unmixing diseased fraction
Thermal | CT, CTD = CT − Tair, NRCT, CWSI | Tstd, MTD (max − min), GLCM | Percentiles

## Slide 20: L2 · Normalisation and scaling: where they belong
FEATURE LEVEL
In MuDAS-AI: SNV, indices and CTD are computed before concatenation (no leakage); z-score is fitted on training plots only, after concatenation, inside the model pipeline.
Bohnenkamp et al. (2019) SNV; Feng et al. (2022) CTD/NRCT; Varma & Simon (2006) leakage; scikit-learn Pipeline practice.
Operation | Acts on | Purpose | Stage | Leakage risk
Radiometric calibration | Image | Physical units | Pre-processing, per flight | None
SNV, derivatives, indices | Row (one spectrum) | Remove brightness / geometry | Feature extraction, per sensor | None
CTD, NRCT, CWSI | Row / flight | Remove weather effect | Feature extraction, per flight | None
z-score / min–max | Column (one feature) | Common scale for SVM, KNN, LASSO, NN | After concatenation, inside training folds | High if fitted on all data
Block scaling (÷√p per sensor) | Feature block | Equal weight per sensor | Optional, inside folds | Same as above

## Slide 21: L2 · Concatenation + selection: the MuDAS-AI Phases 1–3
FEATURE LEVEL · ML
In MuDAS-AI: Phase 3 is your feature-level ML fusion model; the same selected features feed decision-level and DL comparisons.
Tian et al. (2021) DSF + ML-SFFS; Mustafa et al. (2023) Boruta + VIF + ML-SFFS; Pudil et al. (1994) SFFS; Kursa & Rudnicki (2010) Boruta.
Phase 1 · Disease-specific features (per sensor)
Phase 2 · VIF/SPA → ML-SFFS → RF/SVM/KNN (per sensor)
Phase 3 · Concatenate DSFs → VIF → ML-SFFS → RF/SVM/KNN
Phase 1 (filter + embedded)
Kruskal–Wallis + FDR (≥ 2 dates)
JM distance
ReliefF, RF importance, Boruta
Stability over half-samples
Phase 2 (single sensor)
VIF < 10 (SPA for HS bands)
ML-SFFS + one-SE rule
Tune RF, SVM, KNN
Baseline per sensor
Phase 3 (fusion)
Concatenate DSFs of chosen sensors
VIF across sensors
ML-SFFS → optimal fused set
15 sensor combinations

## Slide 22: L2 · Feature selection: filter, wrapper, embedded
FEATURE LEVEL · ML
In MuDAS-AI: use filters first (fast), embedded methods for model-based relevance, and the ML-SFFS wrapper last; add LASSO / elastic net as a fast baseline.
Guyon & Elisseeff (2003); Kononenko (1994) ReliefF; Pudil et al. (1994); Tibshirani (1996) LASSO; Kursa & Rudnicki (2010); Shafiee et al. (2021) SFS vs LASSO.
Family | Principle | Examples | Pros | Cons
Filter | Score each feature with a statistic, no model | Kruskal–Wallis + FDR, JM distance, ReliefF, mutual information, VIF | Fast, model-independent | Ignores interactions (except ReliefF)
Wrapper | Search subsets using a model's CV score | SFS, SFFS, RFE, genetic algorithms, SPA-LDA | Optimal subset for that model | Slow, overfits without nested CV
Embedded | Selection inside model training | LASSO, elastic net, RF importance, Boruta, L1-SVM | Fast, uses the model | Model-specific

## Slide 23: L2 · Subspace fusion: PCA, PLS and canonical correlation
FEATURE LEVEL · ML
In MuDAS-AI: PLS-DA/PLSR on fused features is a strong interpretable baseline; CCA can show which MS/HS features co-vary with thermal features. Fit all transforms within training folds.
Hotelling (1936) CCA; Haghighat et al. (2016) discriminant correlation analysis; Wold et al. (2001) PLS; Zhang et al. (2012) PLSR.
PCA (unsupervised)
Projects concatenated features onto orthogonal components
Removes redundancy, reduces dimension
Components may not relate to disease
No labels → can be fitted without leakage if done on unlabeled data only
PLS / PLS-DA (supervised)
Latent variables maximise covariance with DI / class
Handles many correlated features with few samples
Loadings show which sensor features matter
Classic in spectroscopy
CCA / DCA (two sensors)
CCA: projections of sensor A and B with maximal correlation
DCA: adds class separation (discriminant)
Fused vector = concatenation or sum of projections
Coordinated representation (Baltrušaitis)

## Slide 24: L2 · Kernel fusion: composite kernels and MKL
FEATURE LEVEL · ML
In MuDAS-AI: one kernel per sensor gives an SVM fusion model whose learned weights μ_s show each sensor's contribution, an alternative to plain concatenation for few samples.
Camps-Valls et al. (2006) composite kernels; Gönen & Alpaydın (2011) multiple kernel learning; Cortes & Vapnik (1995) SVM.
K_fused(xᵢ, xⱼ) = Σₛ μₛ · Kₛ(xᵢˢ, xⱼˢ), μₛ ≥ 0, Σₛ μₛ = 1 (s = RGB, MS, HS, TIR)
How
Compute a separate kernel (e.g. RBF) on each sensor's features
Composite kernel: fixed weights μₛ chosen by inner CV
MKL: μₛ learned jointly with the SVM
Each sensor can have its own kernel width γₛ
Why
Avoids one sensor dominating because it has more features
Weights are interpretable as sensor importance
Works well with small sample sizes (kernel methods)
Python: custom kernel in scikit-learn SVC, or MKL libraries

## Slide 25: L2 · ML classifiers for fused features (severity classes and DI)
FEATURE LEVEL · ML
In MuDAS-AI: RF, SVM and KNN are your main classifiers; add PLS-DA / LDA and an ordinal or regression model as interpretable baselines.
Breiman (2001) RF; Cortes & Vapnik (1995) SVM; Chen & Guestrin (2016) XGBoost; Tibshirani (1996); Cao et al. (2020) ordinal; Shafiee et al. (2021).
Model | Type | Good for | Watch out
Random forest | Ensemble of trees | Mixed features, interactions, small data; importance | Less smooth class boundaries
SVM (RBF) | Kernel max-margin | High-dimensional, few samples; one-vs-one for 6 classes | Needs scaling; tune C, γ
KNN | Instance-based | Simple, local patterns | Needs scaling; sensitive to irrelevant features
XGBoost / LightGBM | Boosted trees | Strong on tabular data | Overfits with few plots; tune carefully
LDA / PLS-DA | Linear latent | Interpretable, collinear features | Linear boundaries
Ordinal / regression (DI) | Cumulative logit, PLSR, SVR, RF-R | Ordered classes; continuous DI | Report R², RMSE

## Slide 26: L2 · What feature-level fusion studies found
LITERATURE · ML FUSION
In MuDAS-AI: expect complementary gains from thermal and texture on top of spectral features, but test each addition; 'more sensors' is not automatically better (Mahlein et al., 2019).
Maimaitijiang et al. (2020); Feng et al. (2022); Liu et al. (2024); Mustafa et al. (2023); Mahlein et al. (2019); Zarco-Tejada et al. (2018).
Study | Sensors / scale | Fusion | Key result
Maimaitijiang et al. 2020 | UAV RGB + MS + thermal; soybean yield | Features concatenated; PLSR, SVR, RFR, DNN | All modalities best (R² ≈ 0.72); fusion reduced spatial error clustering
Feng et al. 2022 | Proximal HS + thermal + RGB; wheat powdery mildew | VI + temperature + texture; PLSR, SVR, RFR | VI+TP+TF best with RFR (R² = 0.872 calibration, 0.862 validation)
Liu et al. 2024 | UAV MS + thermal; wheat powdery mildew | Percentile spectra + texture index + CT; MLR | Percentile spectra + TTCI + CT best (R² = 0.90, RMSE 8.28 %)
Mustafa et al. 2023 | HS + fluorescence + phenotyping; wheat FHB | Feature selection + SFFS; KNN, SVM | Small fused feature sets improved detection from the asymptomatic stage
Mahlein et al. 2019 | Thermal + fluorescence + HS; spikelets | Combined parameters; SVM | Single sensors 78/56/78 % (3 dai); IRT–HSI or CFI–HSI 89 % (30 dai)
Zarco-Tejada et al. 2018 | Airborne HS + thermal; olive Xylella | Plant traits; ML classification | Fluorescence + thermal + pigment traits: > 80 % accuracy; pre-visual detection

## Slide 27: DL fusion: early, intermediate and late in neural networks
DEEP LEARNING · OVERVIEW
In MuDAS-AI: test all three DL fusion types on the same tiles and folds; intermediate fusion with sensor-specific encoders is the expected main model.
Ngiam et al. (2011); Ramachandram & Taylor (2017); Baltrušaitis et al. (2019); Hong et al. (2021); Audebert et al. (2018).
DL fusion type | Where sensors meet | Architecture | Needs
Early (input) | At the first layer | Stacked channels → one CNN | Common grid, precise co-registration
Intermediate (feature) | Inside the network | One encoder per sensor → concat / attention → head | More parameters; staged training
Late (decision) | At the outputs | Separate networks → averaged / stacked predictions | Calibrated probabilities
Cross / attention | Repeatedly between branches | Cross-attention, feature exchange at several depths | More data or pre-training
Hong et al. (2021) compared early, middle, late, encoder–decoder and cross fusion: middle and late beat early; cross fusion was best; early fusion collapsed when a modality was missing at test time.

## Slide 28: DL early fusion: stacked-channel CNN
DEEP LEARNING · EARLY
In MuDAS-AI: Experiment: 64 × 64 tiles from the 5 cm common stack (RGB + MS + HS-PCA + TIR = ~29 channels) → small CNN or HybridSN → plot class via tile aggregation.
Audebert et al. (2018) early (FuseNet-type) vs late fusion; Hong et al. (2021); Roy et al. (2020) HybridSN for spectral–spatial cubes.
[RGB(3) | MS(5) | HS-PCA(20) | TIR(1)] → 29-channel tile → Conv layers → pooled features → ordinal head
Pros
Simplest DL fusion; one network
Can learn pixel-level cross-sensor interactions
Direct counterpart of pixel stacking (L1)
Cons
Forces all sensors to one resolution (loses RGB detail or upsamples thermal)
Sensitive to misregistration
Sensor with many channels (HS) can dominate
Sensitive to missing data (Audebert et al., 2018)

## Slide 29: DL intermediate fusion: multi-branch encoders
DEEP LEARNING · INTERMEDIATE
In MuDAS-AI: main DL model: pre-trained ResNet-18 (RGB), small CNNs (MS, TIR), 1D/3D CNN (HS); fused embeddings → ordinal head + DI head.
Maimaitijiang et al. (2020) DNN-F2 (intermediate) > DNN-F1 (input); Kerkech et al. (2020b) VddNet parallel encoders RGB + NIR + depth; Hong et al. (2021).
RGB → ResNet-18
MS → small CNN
HS → 1D/3D-CNN
TIR → small CNN
Concat / attention
Ordinal + DI heads
Why it works
Each sensor gets an encoder suited to its data and native resolution
Fusion of learned features captures cross-sensor interactions
Ablation = drop a branch; pre-trained single-sensor encoders can be reused
Evidence
Maimaitijiang 2020: intermediate DNN best, but gain over RF small (~950 plots)
VddNet (Kerkech 2020b): encoders per input fused at several stages, for vine disease segmentation
Hong 2021: middle fusion > early fusion

## Slide 30: DL attention, gating and cross-modal fusion
DEEP LEARNING · ATTENTION
In MuDAS-AI: gating weights per sensor and per date can show, e.g., thermal dominating early and RGB texture dominating late; report them as interpretability results.
Hu et al. (2018) squeeze-and-excitation; Vaswani et al. (2017) attention; Hong et al. (2021) cross fusion; Hong et al. (2022) SpectralFormer.
Gated fusion: z = Σₛ αₛ · fₛ , αₛ = softmax_s( wᵀ tanh(W fₛ) ) (fₛ: embedding of sensor s)
Sensor gating
Learns a weight per sensor for each sample
Interpretable; few extra parameters
Channel attention
Squeeze-and-excitation reweights channels/bands inside an encoder
Useful in the HS branch (band importance)
Cross-attention
One sensor's features query another's (e.g. HS ↔ RGB)
Transformer-style; best in Hong 2021 but data-hungry
Use with self-supervised pre-training

## Slide 31: DL sensor-specific encoders (single-sensor level)
DEEP LEARNING · ENCODERS
In MuDAS-AI: train each encoder as a single-sensor model first (Objective O2); these models are the DL baselines and the initial weights for fusion.
He et al. (2016) ResNet; Roy et al. (2020) HybridSN; Hong et al. (2022) SpectralFormer; Zhang, X. et al. (2019); Shi et al. (2022); Pan et al. (2021).
Sensor | Encoder options | Input | Reference examples
RGB | ResNet-18 / EfficientNet-B0 pre-trained on ImageNet; U-Net/PSPNet for segmentation | 3-channel tiles (≈ 1 cm) | He et al. 2016; Pan et al. 2021
Multispectral | Small 2D-CNN (3–4 conv blocks), optional SE attention | 5 bands (+ indices) | Su et al. 2018 (ML baseline)
Hyperspectral | 1D-CNN on spectra; 3D/2D HybridSN on cubes; SpectralFormer | Full bands or PCA | Roy et al. 2020; Zhang et al. 2019; Shi et al. 2022
Thermal | Small 2D-CNN on CTD/NRCT tiles | 1 channel | —
Structure | Small CNN on canopy height model | 1 channel | Kerkech et al. 2020b (depth branch)

## Slide 32: DL training with few labelled plots
DEEP LEARNING · TRAINING
In MuDAS-AI: 192 plot labels are small for DL: use tiles, pre-trained encoders, staged training, synchronised augmentation and modality dropout, and compare honestly with ML.
Neverova et al. (2016) ModDrop; Wang, Tran & Feiszli (2020) modality imbalance; He et al. (2022) masked autoencoders; Maimaitijiang et al. (2020) sample-size caution.
Data
Tiles per plot (each inherits the plot label)
Synchronised augmentation: same flip/rotation/crop for all sensors
Small per-sensor radiometric jitter
Class weights / balanced sampling
Model
ImageNet weights for RGB
Self-supervised pre-training (MAE / contrastive) on unlabelled tiles of all flights
Small encoders, dropout, weight decay
Staged: train branches → freeze → train fusion head → fine-tune
Fusion-specific
Modality dropout: randomly zero one sensor (p ≈ 0.1–0.2)
Watch modality imbalance: one sensor learns fastest and others are ignored
Early stopping on inner folds
3–5 seeds; report mean ± SD

## Slide 33: DL with plot-level labels: tiles, MIL and label proportions
DEEP LEARNING · WEAK LABELS
In MuDAS-AI: attention-MIL gives one plot prediction and a within-plot attention map that can be compared with the hotspot analysis (Moran's I, Gi*).
Ilse et al. (2018) attention-based MIL; Quadrianto et al. (2009) learning from label proportions; Cao et al. (2020) CORAL ordinal regression.
Attention MIL: z_plot = Σᵢ aᵢ hᵢ , aᵢ = softmax(wᵀ tanh(V hᵢ)) Label proportion: mean(pᵢ) ≈ DI_plot / 100
Tile inheritance
Simplest: every tile gets the plot class
Average tile predictions per plot
Noisy for low-DI plots
Attention MIL
Plot = bag of tiles; only bag label known
Learns which tiles matter
Weights → within-plot map
Ordinal output
CORAL: K − 1 binary 'severity > k' outputs
Respects class order; fewer large errors
Add DI regression head (multi-task)

## Slide 34: L3 · Decision-level fusion: concept and combination rules
DECISION LEVEL
In MuDAS-AI: combine the four single-sensor models from Phase 2 (ML) or the DL single-sensor networks; the result is a robust ensemble that still works if a sensor fails on a date.
Kittler et al. (1998) combining classifiers; Platt (1999) probability calibration; Snoek et al. (2005) early vs late fusion.
Rule | Formula | Comment
Majority vote | ŷ = mode(ŷ_RGB, ŷ_MS, ŷ_HS, ŷ_TIR) | Uses labels only; ties possible with 4 sensors
Sum / mean rule | P(c) = (1/S) Σₛ Pₛ(c) | Robust; needs calibrated probabilities
Weighted mean | P(c) = Σₛ wₛ Pₛ(c), weights from inner-CV accuracy | Rewards reliable sensors
Product rule | P(c) ∝ Πₛ Pₛ(c) | Assumes independence; sensitive to one near-zero
Max / min rule | Largest / smallest support | Rarely best
Calibrate probabilities first (Platt scaling for SVM; isotonic or temperature scaling for others) because sensor models produce scores on different scales.

## Slide 35: L3 · Stacking, Bayesian and Dempster–Shafer fusion
DECISION LEVEL
In MuDAS-AI: stacking (meta-model on out-of-fold sensor probabilities) is easy to implement with scikit-learn and must be nested inside the plot-grouped CV.
Wolpert (1992) stacked generalization; Shafer (1976) evidence theory; Kittler et al. (1998); Varma & Simon (2006).
Stacking
Level-0: one model per sensor
Collect out-of-fold probabilities on training plots
Level-1: logistic regression / small RF learns how to combine
Fitted only inside training folds
Bayesian / naive Bayes
Treat sensor outputs as evidence; combine posteriors with priors
Simple if independence is acceptable
Gives probabilities for maps
Dempster–Shafer
Each sensor assigns belief to classes and to 'uncertain'
Combination rule handles conflict and ignorance
Useful when a sensor is unreliable on some dates

## Slide 36: L3 · Late fusion in deep learning: examples
DECISION LEVEL · DL
In MuDAS-AI: late DL fusion (average of single-sensor network probabilities) is the robustness baseline against which intermediate fusion must show a gain.
Kerkech et al. (2020a) Comput. Electron. Agric. 174:105446; Audebert et al. (2018) ISPRS J. 140:20–32; Hong et al. (2021).
Kerkech et al. 2020a: vine disease (UAV)
Iterative keypoint registration of visible and infrared images
SegNet segments each image separately: shadow, ground, healthy, symptomatic
Segmentations fused into one disease map (decision level)
Reported > 92 % detection at grapevine level, 87 % at leaf level
Audebert et al. 2018 / Hong et al. 2021
Late fusion corrects errors from ambiguous data and is robust to missing data
Early fusion learns joint features but is sensitive to missing modalities
Hong 2021: middle and cross fusion > early fusion
Lesson: compare levels; combine where useful (hybrid)

## Slide 37: Hybrid fusion: combining levels
HYBRID
In MuDAS-AI: a practical hybrid: ensemble of the best feature-level ML model (Phase 3) and the best intermediate-fusion DL model; test whether it beats both.
Hong et al. (2021) cross fusion; Kerkech et al. (2020b) multi-stage fusion; Wolpert (1992); Pohl & Van Genderen (1998).
Hybrid design | Example | When useful
Feature fusion within groups + decision fusion across | Optical (RGB+MS+HS) feature model + thermal model → stacked | Thermal on a different grid or missing on some dates
Pixel fusion + feature fusion | Sharpen thermal with NDVI (L1), then plot features (L2) | Thermal too coarse for small plots
Multi-stage DL fusion | Encoders exchange features at several depths | Enough data / pre-training
ML + DL ensemble | Average probabilities of Phase 3 RF and DL fusion net | Models make different errors

## Slide 38: Comparison of fusion levels for UAV disease severity
COMPARISON
In MuDAS-AI: feature-level ML (Phase 3) is the primary method; intermediate DL and decision-level fusion are the main comparisons; pixel-level fusion is an optional enhancement.
Pohl & Van Genderen (1998); Gómez-Chova et al. (2015); Hong et al. (2021); Maimaitijiang et al. (2020).
Level | Co-registration need | Data need | Interpretability | Missing sensor | Fit for MuDAS-AI
L1 pixel (image fusion / early CNN) | Very high | High (pixel labels or many tiles) | Low–medium | Fails | Optional / exploratory
L2 feature, ML | Moderate (plot-level) | Low–moderate | High | Retrain without it | Primary
L2 feature, DL intermediate | Moderate–high | Moderate–high | Medium (attention) | Modality dropout helps | Main DL comparison
L3 decision | Low | Low | High (per-sensor) | Robust | Robust baseline
Hybrid | Varies | Varies | Medium | Robust | Final ensemble test

## Slide 39: What the evidence says: lessons for the design
LITERATURE · LESSONS
In MuDAS-AI: design the thesis as a fair comparison: same plots, same folds, same metrics, paired tests; a 'no gain from fusion' result is publishable if the test is fair.
Hong et al. (2021); Audebert et al. (2018); Maimaitijiang et al. (2020); Mahlein et al. (2019); Feng et al. (2022); Bohnenkamp et al. (2019); Roberts et al. (2017).
Lessons
Middle/cross > early fusion; late more robust (Hong 2021; Audebert 2018)
DL gain over ML is small with few samples (Maimaitijiang 2020)
More sensors ≠ always better: test combinations (Mahlein 2019)
Thermal + spectral + texture complement each other (Feng 2022; Liu 2024)
Pitfalls seen in papers
Pixel-level random splits inflate accuracy (Roberts 2017)
Feature selection on all data before CV (several studies) → optimistic
Features selected at one scale may not transfer (Bohnenkamp 2019)
No paired test between fusion and single sensor

## Slide 40: Validation design for fusion experiments
VALIDATION
In MuDAS-AI: the same outer folds are used for every single-sensor, fusion-level and ML/DL model, so all results are paired and directly comparable.
Varma & Simon (2006) nested CV; Roberts et al. (2017) structured CV; Foody (2004) McNemar for map accuracy; Olofsson et al. (2014).
Outer: 4 folds grouped by plot (testing)
Inner: 4 folds (selection, tuning, early stopping)
Repeat ×3 seeds
Leave-one-date-out
External: Bharatpur (frozen)
Metric | Why
Macro-F1, OA, quadratic-weighted kappa | Class imbalance; ordered classes
Confusion matrix; per-class recall/precision | Where errors occur (e.g. class 4 vs 5)
Healthy-vs-diseased sensitivity | Early detection relevance
R², RMSE, RPD (DI regression) | Continuous severity
McNemar (paired predictions) | Is fusion significantly better?

## Slide 41: Ablation, fusion gain and interpretation
VALIDATION · INTERPRETATION
In MuDAS-AI: the 15-combination ablation answers Objective O4 (cheapest adequate sensor set); interpretation links selected features to white rust physiology.
Breiman (2001) permutation importance; Selvaraju et al. (2017) Grad-CAM; Gönen & Alpaydın (2011) MKL weights; Ilse et al. (2018).
Fusion gain = score(fused) − max_s score(single sensor s) · Combinations for 4 sensors = 2⁴ − 1 = 15
Ablation
All 15 combinations × each fusion level
Report mean ± SD over repeats
McNemar: best single vs best fused; each triple vs all four
Plot accuracy vs number/cost of sensors
Interpretation
ML: selected features, permutation importance, partial dependence
Kernel: MKL sensor weights μₛ
DL: gating weights, Grad-CAM per branch, spectral attributions, MIL attention maps
Check physiological plausibility (chlorophyll, transpiration, texture)

## Slide 42: End-to-end workflow: acquisition → fusion → model → map
PRACTICAL FLOW
In MuDAS-AI: each box corresponds to a pipeline step or script; follow the order and do not skip the QA checks between steps.
Synthesis of this deck; pipeline modules s01–s08 (MuDAS-AI).
1 Plan & fly
Same-day flights, GCPs, panels, thermal refs
2 Ground truth
DI by layer & surface; metadata
3 Calibrate
Reflectance, °C, CTD
4 Co-register
Same GCPs + fine alignment; RMSE check
5 Mask & grid
Canopy/shadow/flower mask; plot inset; optional stack
6 Features
Per sensor: indices, texture, thermal, structure
7 Phase 1
Disease-specific features per sensor
8 Phase 2
Single-sensor ML models (baselines)
9 Fusion
Feature-level ML (Phase 3), decision-level, DL
10 Validate
Nested plot-grouped CV, McNemar, ablation
11 External
Frozen model at Bharatpur; farmer fields
12 Map
Severity map → spray zones; uncertainty

## Slide 43: Easy-to-perform recipe: feature-level fusion in Python
PRACTICAL FLOW · CODE LOGIC
In MuDAS-AI: this recipe is what run_nested() in s07_models.py implements; run it once per sensor combination and fusion level.
scikit-learn Pipeline, GroupKFold / StratifiedGroupKFold; mlxtend SequentialFeatureSelector (floating=True); Pudil et al. (1994).
for each outer fold (StratifiedGroupKFold, groups = plot_id):
train, test = split(table) # all dates of a plot together
for each sensor s: dsf[s] = phase1(train[s]) # KW+FDR, JM, ReliefF, Boruta
X = concat(train[dsf[s]] for s in combination) # feature-level fusion
X = vif_filter(X) # remove redundancy
pipe = Pipeline([impute, StandardScaler(), clf]) # scaler fitted on training only
ofc = SFFS(pipe, X, y, cv=GroupKFold(inner)) # optimal feature combination
model = GridSearchCV(pipe, grid, cv=inner).fit(X[ofc], y)
predictions[test] = model.predict(test[ofc]) # test plots used once
report macro-F1, kappa, confusion matrix; McNemar vs single-sensor models

## Slide 44: Recommended experiment plan for the thesis
PRACTICAL FLOW · EXPERIMENTS
In MuDAS-AI: Experiments E1–E4 are essential; E5–E8 strengthen the thesis if time and data allow.
Design follows Hong et al. (2021) fusion comparison and Maimaitijiang et al. (2020) ML vs DL comparison, with nested plot-grouped validation (Varma & Simon, 2006).
Exp. | Fusion level / method | Models | Objective
E1 | Single sensor (no fusion), features + Phase 1–2 | RF, SVM, KNN | O1, O2 baselines
E2 | Feature-level ML fusion (Phase 3), 15 combinations | RF, SVM, KNN + LASSO/PLS-DA baselines | O3, O4
E3 | Decision-level fusion of E1 models | Weighted mean, stacking | O3 robustness
E4 | Validation: leave-one-date-out + Bharatpur external | Best of E2/E3 | Transferability
E5 | Kernel-level fusion (composite kernel / MKL) | SVM | Sensor weights
E6 | DL single-sensor + intermediate fusion (+ attention MIL) | Multi-branch CNN | ML vs DL
E7 | DL early and late fusion | Stacked CNN; averaged nets | Fusion-level comparison
E8 | Pixel-level fusion (thermal sharpening / HS–RGB) for hotspot maps | TsHARP, MRA; quality metrics | Within-plot maps

## Slide 45: Outputs to report for each experiment
PRACTICAL FLOW · REPORTING
In MuDAS-AI: these tables and figures map directly onto Results chapter sections: single-sensor, fusion comparison, interpretation, transferability, maps.
Reporting practice: Olofsson et al. (2014); Foody (2004); Roberts et al. (2017).
Tables
Feature list per sensor (Phase 1)
Single-sensor results (E1)
15-combination fusion table (E2/E3)
Fusion-level comparison with McNemar
External test (Bharatpur)
Figures
Workflow diagram
Confusion matrices (best single vs best fused)
Accuracy vs number of sensors / cost
Permutation importance; gating weights
Severity maps per date
Quality statements
Co-registration RMSE per sensor/date
Calibration checks
Class distribution per date
Limitations: plot-level labels, one season, leaf-underside symptoms

## Slide 46: Checklist: common mistakes in multimodal fusion studies
PRACTICAL FLOW · CHECKLIST
In MuDAS-AI: go through this list before submitting a chapter or paper.
Su et al. (2018); Varma & Simon (2006); Roberts et al. (2017); Wang, Tran & Feiszli (2020); Bohnenkamp et al. (2019).
✗ Sensors flown on different days or far apart in time
✗ No co-registration check (thermal shifted by several pixels)
✗ Raw canopy temperature used across dates (weather confounds disease)
✗ Scaling or feature selection fitted on all plots before CV (leakage)
✗ Pixels or tiles of one plot in both training and test
✗ Fusion compared with single sensors without a paired test
✗ One sensor dominating because it has many more features
✗ DL claimed better without the same folds as ML
✗ Pixel-level maps claimed without pixel-level validation
✗ Leaf-underside symptoms ignored in ground truth

## Slide 47: References (1/4)
REFERENCES
Agam, N., Kustas, W.P., Anderson, M.C., Li, F., Neale, C.M.U. (2007). A vegetation index based technique for spatial sharpening of thermal imagery. Remote Sens. Environ. 107, 545–558.
Alparone, L., et al. (2008). Multispectral and panchromatic data fusion assessment without reference. Photogramm. Eng. Remote Sens. 74(2), 193–200.
Audebert, N., Le Saux, B., Lefèvre, S. (2018). Beyond RGB: very high resolution urban remote sensing with multimodal deep networks. ISPRS J. Photogramm. Remote Sens. 140, 20–32.
Baltrušaitis, T., Ahuja, C., Morency, L.-P. (2019). Multimodal machine learning: a survey and taxonomy. IEEE TPAMI 41(2), 423–443.
Bohnenkamp, D., Behmann, J., Mahlein, A.-K. (2019). In-field detection of yellow rust in wheat on the ground canopy and UAV scale. Remote Sens. 11(21), 2495.
Breiman, L. (2001). Random forests. Machine Learning 45, 5–32.
Camps-Valls, G., et al. (2006). Composite kernels for hyperspectral image classification. IEEE GRSL 3(1), 93–97.
Cao, W., Mirjalili, V., Raschka, S. (2020). Rank consistent ordinal regression for neural networks. Pattern Recognit. Lett. 140, 325–331.
Castanedo, F. (2013). A review of data fusion techniques. Sci. World J. 2013, 704504.
Chen, T., Guestrin, C. (2016). XGBoost: a scalable tree boosting system. Proc. KDD, 785–794.
Cortes, C., Vapnik, V. (1995). Support-vector networks. Machine Learning 20, 273–297.
Evangelidis, G.D., Psarakis, E.Z. (2008). Parametric image alignment using enhanced correlation coefficient maximization. IEEE TPAMI 30(10), 1858–1865.
Feng, Z., et al. (2022). Monitoring wheat powdery mildew based on hyperspectral, thermal infrared, and RGB image data fusion. Sensors 22(1), 31.
Foody, G.M. (2004). Thematic map comparison: evaluating the statistical significance of differences in classification accuracy. Photogramm. Eng. Remote Sens. 70(5), 627–633.
Ghassemian, H. (2016). A review of remote sensing image fusion methods. Information Fusion 32, 75–89.
Gómez-Chova, L., Tuia, D., Moser, G., Camps-Valls, G. (2015). Multimodal classification of remote sensing images: a review and future directions. Proc. IEEE 103(9), 1560–1584.
Gönen, M., Alpaydın, E. (2011). Multiple kernel learning algorithms. J. Mach. Learn. Res. 12, 2211–2268.
Guo, A., et al. (2021). Wheat yellow rust detection using UAV-based hyperspectral technology. Remote Sens. 13(1), 123.
Guyon, I., Elisseeff, A. (2003). An introduction to variable and feature selection. J. Mach. Learn. Res. 3, 1157–1182.
Haghighat, M., Abdel-Mottaleb, M., Alhalabi, W. (2016). Discriminant correlation analysis: real-time feature level fusion for multimodal biometric recognition. IEEE Trans. Inf. Forensics Secur. 11(9), 1984–1996.
Hall, D.L., Llinas, J. (1997). An introduction to multisensor data fusion. Proc. IEEE 85(1), 6–23.

## Slide 48: References (2/4)
REFERENCES
He, K., Zhang, X., Ren, S., Sun, J. (2016). Deep residual learning for image recognition. Proc. CVPR, 770–778.
He, K., et al. (2022). Masked autoencoders are scalable vision learners. Proc. CVPR, 16000–16009.
Hong, D., et al. (2021). More diverse means better: multimodal deep learning meets remote-sensing imagery classification. IEEE TGRS 59(5), 4340–4354.
Hong, D., et al. (2022). SpectralFormer: rethinking hyperspectral image classification with transformers. IEEE TGRS 60, 5518615.
Hotelling, H. (1936). Relations between two sets of variates. Biometrika 28, 321–377.
Hu, J., Shen, L., Sun, G. (2018). Squeeze-and-excitation networks. Proc. CVPR, 7132–7141.
Ilse, M., Tomczak, J., Welling, M. (2018). Attention-based deep multiple instance learning. Proc. ICML, 2127–2136.
Jones, H.G. (2004). Application of thermal imaging and infrared sensing in plant physiology and ecophysiology. Adv. Bot. Res. 41, 107–163.
Kerkech, M., Hafiane, A., Canals, R. (2020a). Vine disease detection in UAV multispectral images using optimized image registration and deep learning segmentation approach. Comput. Electron. Agric. 174, 105446.
Kerkech, M., Hafiane, A., Canals, R. (2020b). VddNet: vine disease detection network based on multispectral images and depth map. Remote Sens. 12(20), 3305.
Kittler, J., Hatef, M., Duin, R.P.W., Matas, J. (1998). On combining classifiers. IEEE TPAMI 20(3), 226–239.
Kononenko, I. (1994). Estimating attributes: analysis and extensions of RELIEF. Proc. ECML-94, LNCS 784, 171–182.
Kursa, M.B., Rudnicki, W.R. (2010). Feature selection with the Boruta package. J. Stat. Softw. 36(11), 1–13.
Lahat, D., Adali, T., Jutten, C. (2015). Multimodal data fusion: an overview of methods, challenges, and prospects. Proc. IEEE 103(9), 1449–1477.
Leinonen, I., Jones, H.G. (2004). Combining thermal and visible imagery for estimating canopy temperature and identifying plant stress. J. Exp. Bot. 55, 1423–1431.
Li, H., Wu, X.-J. (2019). DenseFuse: a fusion approach to infrared and visible images. IEEE Trans. Image Process. 28(5), 2614–2623.
Liu, Y., et al. (2024). Exploring multi-features in UAV based optical and thermal infrared images to estimate disease severity of wheat powdery mildew. Comput. Electron. Agric. 225, 109285.
Lowe, D.G. (2004). Distinctive image features from scale-invariant keypoints. Int. J. Comput. Vis. 60, 91–110.
Ma, J., Ma, Y., Li, C. (2019). Infrared and visible image fusion methods and applications: a survey. Information Fusion 45, 153–178.
Maes, F., et al. (1997). Multimodality image registration by maximization of mutual information. IEEE Trans. Med. Imaging 16(2), 187–198.
Mahlein, A.-K. (2016). Plant disease detection by imaging sensors. Plant Dis. 100(2), 241–251.

## Slide 49: References (3/4)
REFERENCES
Mahlein, A.-K., et al. (2019). Comparison and combination of thermal, fluorescence, and hyperspectral imaging for monitoring Fusarium head blight of wheat on spikelet scale. Sensors 19(10), 2281.
Maimaitijiang, M., et al. (2020). Soybean yield prediction from UAV using multimodal data fusion and deep learning. Remote Sens. Environ. 237, 111599.
McKinney, H.H. (1923). Influence of soil temperature and moisture on infection of wheat seedlings by Helminthosporium sativum. J. Agric. Res. 26, 195–218.
Mustafa, G., et al. (2023). Fusarium head blight monitoring in wheat ears using machine learning and multimodal data from asymptomatic to symptomatic periods. Front. Plant Sci. 13, 1102341.
Neverova, N., Wolf, C., Taylor, G., Nebout, F. (2016). ModDrop: adaptive multi-modal gesture recognition. IEEE TPAMI 38(8), 1692–1706.
Ngiam, J., et al. (2011). Multimodal deep learning. Proc. ICML, 689–696.
Olofsson, P., et al. (2014). Good practices for estimating area and assessing accuracy of land change. Remote Sens. Environ. 148, 42–57.
Pan, Q., et al. (2021). A deep-learning-based approach for wheat yellow rust disease recognition from unmanned aerial vehicle images. Sensors 21(19), 6540.
Platt, J. (1999). Probabilistic outputs for support vector machines and comparisons to regularized likelihood methods. In: Advances in Large Margin Classifiers, MIT Press.
Pohl, C., Van Genderen, J.L. (1998). Multisensor image fusion in remote sensing: concepts, methods and applications. Int. J. Remote Sens. 19(5), 823–854.
Pudil, P., Novovičová, J., Kittler, J. (1994). Floating search methods in feature selection. Pattern Recognit. Lett. 15, 1119–1125.
Quadrianto, N., Smola, A.J., Caetano, T.S., Le, Q.V. (2009). Estimating labels from label proportions. J. Mach. Learn. Res. 10, 2349–2374.
Ramachandram, D., Taylor, G.W. (2017). Deep multimodal learning: a survey on recent advances and trends. IEEE Signal Process. Mag. 34(6), 96–108.
Roberts, D.R., et al. (2017). Cross-validation strategies for data with temporal, spatial, hierarchical, or phylogenetic structure. Ecography 40, 913–929.
Ronneberger, O., Fischer, P., Brox, T. (2015). U-Net: convolutional networks for biomedical image segmentation. Proc. MICCAI, 234–241.
Roy, S.K., et al. (2020). HybridSN: exploring 3-D–2-D CNN feature hierarchy for hyperspectral image classification. IEEE GRSL 17(2), 277–281.
Selvaraju, R.R., et al. (2017). Grad-CAM: visual explanations from deep networks via gradient-based localization. Proc. ICCV, 618–626.
Shafer, G. (1976). A Mathematical Theory of Evidence. Princeton University Press.
Shafiee, S., et al. (2021). Sequential forward selection and support vector regression in comparison to LASSO regression for spring wheat yield prediction based on UAV imagery. Comput. Electron. Agric. 183, 106036.
Shi, Y., et al. (2022). Novel CropdocNet model for automated potato late blight disease detection from UAV-based hyperspectral imagery. Remote Sens. 14(2), 396.
Snoek, C.G.M., Worring, M., Smeulders, A.W.M. (2005). Early versus late fusion in semantic video analysis. Proc. ACM Multimedia, 399–402.

## Slide 50: References (4/4)
REFERENCES
Su, J., et al. (2018). Wheat yellow rust monitoring by learning from multispectral UAV aerial imagery. Comput. Electron. Agric. 155, 157–166.
Tian, L., et al. (2021). Spectroscopic detection of rice leaf blast infection from asymptomatic to mild stages with integrated machine learning and feature selection. Remote Sens. Environ. 257, 112350.
Tibshirani, R. (1996). Regression shrinkage and selection via the lasso. J. R. Stat. Soc. B 58(1), 267–288.
Varma, S., Simon, R. (2006). Bias in error estimation when using cross-validation for model selection. BMC Bioinformatics 7, 91.
Vaswani, A., et al. (2017). Attention is all you need. Proc. NeurIPS, 5998–6008.
Vivone, G., et al. (2015). A critical comparison among pansharpening algorithms. IEEE TGRS 53(5), 2565–2586.
Wald, L., Ranchin, T., Mangolini, M. (1997). Fusion of satellite images of different spatial resolutions: assessing the quality of resulting images. Photogramm. Eng. Remote Sens. 63(6), 691–699.
Wang, W., Tran, D., Feiszli, M. (2020). What makes training multi-modal classification networks hard? Proc. CVPR, 12695–12705.
Wang, Z., Bovik, A.C., Sheikh, H.R., Simoncelli, E.P. (2004). Image quality assessment: from error visibility to structural similarity. IEEE Trans. Image Process. 13(4), 600–612.
Whetton, R.L., Waine, T.W., Mouazen, A.M. (2018). Hyperspectral measurements of yellow rust and fusarium head blight in cereal crops: Part 2. Biosyst. Eng. 167, 144–158.
Wold, S., Sjöström, M., Eriksson, L. (2001). PLS-regression: a basic tool of chemometrics. Chemom. Intell. Lab. Syst. 58, 109–130.
Wolpert, D.H. (1992). Stacked generalization. Neural Networks 5(2), 241–259.
Yokoya, N., Yairi, T., Iwasaki, A. (2012). Coupled nonnegative matrix factorization unmixing for hyperspectral and multispectral data fusion. IEEE TGRS 50(2), 528–537.
Yokoya, N., Grohnfeldt, C., Chanussot, J. (2017). Hyperspectral and multispectral data fusion: a comparative review of the recent literature. IEEE Geosci. Remote Sens. Mag. 5(2), 29–56.
Zarco-Tejada, P.J., et al. (2018). Previsual symptoms of Xylella fastidiosa infection revealed in spectral plant-trait alterations. Nature Plants 4, 432–439.
Zhang, J.-C., et al. (2012). Detecting powdery mildew of winter wheat using leaf level hyperspectral measurements. Comput. Electron. Agric. 85, 13–23.
Zhang, X., et al. (2019). A deep learning-based approach for automated yellow rust disease detection from high-resolution hyperspectral UAV images. Remote Sens. 11(13), 1554.
Zitová, B., Flusser, J. (2003). Image registration methods: a survey. Image Vis. Comput. 21(11), 977–1000.
Notes: Bibliographic details marked as verified in conversation: Maimaitijiang 2020, Kerkech 2020a/b, Hong 2021, Audebert 2018, Feng 2022, Liu 2024, Mustafa 2023, Mahlein 2019, Zarco-Tejada 2018, Bohnenkamp 2019, Guo 2021, Su 2018, Tian 2021, Shafiee 2021, Zhang 2012, Whetton 2018, Pan 2021, Shi 2022, Lahat 2015, Baltrušaitis 2019. Others are standard method references compiled from memory: verify volume/page details before submission.