## Slide 1: Chlorophyll Fluorescence & Sun-Induced Fluorescence
From PSII photophysics and PAM fluorometry to remote sensing of SIF from space — a systematic, diagram-led guide
Chlorophyll extract: green in white light, glowing red under UV
Based on Murchie & Lawson (2013) J. Exp. Bot. 64: 3983–3998 · Mohammed et al. (2019) Remote Sens. Environ. 231: 111177 · course slides on Chl a fluorescence
Notes: This deck builds the topic from the ground up: the physics of how chlorophyll re-emits light, how we measure it actively with PAM fluorometers, how each parameter is derived, the pitfalls, and then how the same signal is measured passively under sunlight (SIF) from towers, drones, aircraft and satellites.

## Slide 2: Roadmap of this deck
01
Foundations
What fluorescence is and where it comes from
02
Measuring it
Ambient light problem, PAM modulation, instruments
03
Induction kinetics
Kautsky effect, OJIP and the slow PSMT phase
04
PSII redox & quenching
Open/closed centres, qP, NPQ, saturating pulse
05
PAM parameters
Fo, Fm, Fv/Fm, ΦPSII, qP, qL, NPQ, worked example
06
Good practice
Dark adaptation, pitfalls, CO₂ link, protocols
07
Imaging & monitoring
Fluorescence imaging, applications, LIFT
08
Sun-induced fluorescence
Spectra, retrieval, models, platforms, satellites
09
Synthesis
Concept map, formula sheet, FAQs, references
Notes: Each module builds on the previous one. If a later slide is confusing, go back to the module it depends on: parameters (05) depend on the open/closed reaction-centre idea (04), and SIF (08) depends on the energy-partitioning idea (01).

## Slide 3: Foundations
What chlorophyll fluorescence is, where it comes from, and why a tiny glow tells us so much about photosynthesis
01
Notes: Key idea of this module: absorbed light energy has three possible fates that compete. Fluorescence is the one we can see, so it reports on the other two.

## Slide 4: What is chlorophyll fluorescence?
Definition: light re-emitted by chlorophyll molecules as they return from the excited to the ground (non-excited) state.
Why it matters
Non-invasive measure of photosystem II (PSII) activity — no harvesting, no chemicals
PSII is highly sensitive to abiotic and biotic factors → a broad indicator of how plants respond to environmental change
Indicator of photosynthetic energy conversion in higher plants, algae and bacteria
Cheap, fast and portable → widely used in plant physiology, breeding and phenotyping
Spectral signature: emission between ~650 and 800 nm with two peaks, ~685 nm (red) and ~740 nm (far-red)
Left: chlorophyll extract in alcohol — green under white light (top), red fluorescence under UV (bottom). Right: absorbed solar energy is dissipated by photochemistry or by non-photochemical routes (heat, fluorescence).
Notes: Definition first. Chlorophyll absorbs light, becomes excited, and a small fraction of that energy is re-emitted as red/far-red light as the molecule returns to its ground state. Because PSII is very sensitive to stress, this re-emission is a cheap, fast, non-invasive window into how the photosynthetic machinery is coping.

## Slide 5: Where does it come from? The pigment–protein complexes
Thylakoid membrane: PSII, cytochrome b₆f, PSI and ATP synthase, with water splitting on the lumen side
Light-harvesting complexes (LHC)
Antenna pigment–protein complexes (Chl a, Chl b, carotenoids) that capture photons and transfer excitation energy to a reaction centre.
Photosystem II (P680)
Core proteins D1, D2, CP43, CP47; splits water (OEC), passes electrons via pheophytin → QA → QB. Main source of variable fluorescence.
Photosystem I (P700)
Receives electrons from plastocyanin and reduces NADP⁺ via ferredoxin. Emits weakly, mostly in the far-red (>700 nm).
Notes: Chlorophyll is not free in the leaf; it is bound to proteins in the thylakoid membrane. The light-harvesting complexes (LHCII, LHCI) act as antennae and funnel excitation energy to the reaction centres P680 (PSII) and P700 (PSI). Fluorescence comes mainly from the PSII antenna and core.

## Slide 6: The photophysics: excitation and emission
S₀
ground state
S₁
lowest excited singlet
S₂
higher excited singlet
T₁ triplet
Blue absorption
~430–450 nm
Red absorption
~660–680 nm
Internal conversion
(heat, femtoseconds)
Fluorescence
650–800 nm
Heat
(NPQ)
¹O₂ risk; quenched by carotenoids
Photochemistry
Three rules that clear most doubts
Excitation colour does not matter: everything relaxes to S₁ first, so emission is always red/far-red (Kasha's rule)
Emission is at longer wavelength than absorption (Stokes shift)
Processes from S₁ compete: the faster one route is, the less goes to the others
Numbers worth remembering
Fluorescence quantum yield in vivo: typically 0.5–3 % (always <10 %)
Fluorescence lifetime: tens to hundreds of picoseconds
Emission peaks: F685 (PSII) and F740 (PSII + PSI)
Charge separation in an open PSII centre is very fast, so photochemistry normally wins
Notes: Why does blue light make red fluorescence? Blue photons lift chlorophyll to the higher excited state S2, which relaxes within femtoseconds to S1 by internal conversion (heat). All useful work and all fluorescence start from the lowest excited singlet S1, so emission is always red, whatever the excitation colour, and it is shifted to longer wavelengths than the red absorption band (Stokes shift). From S1 the energy can go to photochemistry, heat, fluorescence, or into the triplet state, which can form harmful singlet oxygen unless carotenoids quench it.

## Slide 7: Three competing fates of absorbed light energy
Absorbed photon
Chl∗
excited
① Photochemistry rate kP
Drives charge separation in PSII → electron transport → ATP + NADPH → CO₂ assimilation
② Heat (NPQ) rate kN
Safe dissipation of excess energy; photoprotective (ΔpH, PsbS, zeaxanthin)
③ Fluorescence rate kF
Re-emitted as red / far-red light (650–800 nm); the part we measure
The competition rule
ΦP + ΦN + ΦF = 1
ΦF = kF / (kF + kP + kN)
Centres closed → kP ≈ 0 → fluorescence rises
NPQ switched on → kN ↑ → fluorescence falls
So fluorescence reports photochemistry and heat loss indirectly
Analogy: three taps fed by one water tank. Close the photochemistry tap (saturating pulse) and the level in the fluorescence tap jumps — that jump is what PAM fluorometry measures.
Notes: The single most important concept. Because the three routes compete for the same excitation, their yields add up to one. If photochemistry slows (reaction centres closed) or heat dissipation is low, fluorescence rises. If photochemistry or NPQ increases, fluorescence is 'quenched'. Measuring fluorescence under controlled conditions therefore lets us infer the other two.

## Slide 8: Why we treat the signal as coming from PSII
Z-scheme: electrons flow from water through PSII (P680) and PSI (P700) to NADP⁺; herbicides DCMU and paraquat block specific steps
PSII dominates the variable signal
At room temperature, changes in fluorescence are attributed to PSII only
PSI contributes little below 700 nm → ignored in most PAM work
PSII emits at both 685 and 740 nm; PSI mostly at ~740 nm
Why this is useful
Photochemistry supplies the energy (ATP) and reducing power (NADPH) for CO₂ assimilation
Fluorescence yield ⇒ quantum efficiency of PSII photochemistry and heat dissipation
PSII is the most stress-sensitive part of the chain → early warning of stress
Caveat for SIF: far-red SIF also contains PSI emission
Notes: At room temperature the variable part of the fluorescence signal comes from PSII. PSI fluorescence is weak, emitted mostly above 700 nm and does not vary much with the redox state, so with detectors that read below ~700 nm we can ignore it. This becomes important again for SIF because far-red SIF at 740–760 nm includes a PSI contribution.

## Slide 9: Measuring fluorescence
How to see a weak red glow against bright light: modulated (PAM) fluorometry and the instruments used
02
Notes: Problem: fluorescence is weak and red, and ambient light also contains red. Solution: modulate the excitation and detect only the modulated signal.

## Slide 10: The ambient-light problem and the PAM solution
Measuring beam
weak, modulated (µs pulses at a fixed frequency)
Ambient / actinic light
strong but un-modulated (constant)
Detector after lock-in
only fluorescence excited by the beam is kept
Time →
Result: measurements can be made without darkening the leaf. Older non-modulated systems needed darkness or tightly controlled light. Non-modulated devices are returning for fast OJIP transients from a 1 s pulse on dark-adapted leaves.
Measuring light (ML)
Too weak to drive electron transport, but enough to excite Fo
Actinic light (AL)
Drives photosynthesis (photochemistry); the leaf's 'working' light
Saturating pulse (SP)
Very bright (≥4000 µmol m⁻² s⁻¹), <1 s; closes all PSII centres → Fm, Fm′
Far-red light (FR)
Excites PSI preferentially, drains electrons from QA/PQ → accurate Fo′
Notes: Pulse-amplitude modulation: the measuring beam is switched on and off at a known frequency. A lock-in detector only amplifies signal at that frequency, so steady sunlight or actinic light (which is not modulated) is ignored. That is why modern PAM measurements can be done in daylight without darkening the leaf. The three other light sources are used to manipulate the photosynthetic state.

## Slide 11: Instruments: from leaf clips to imaging systems
Dark-adaptation leaf clips
Hand-held fluorometer on a leaf
Laboratory chlorophyll fluorescence imaging system
Imaging head and Ft image of a leaf surface
Modulated (PAM) fluorometers
Work in light or dark; full quenching analysis (Fv/Fm, ΦPSII, NPQ, qP)
Large, well-tested physiological framework
Continuous-excitation (OJIP) meters
Fast induction transient during a 1 s pulse on dark-adapted leaves
Popular for screening; complex derived parameters need caution
Notes: All of these use the same principles. Hand-held PAM or OJIP meters measure a small spot; leaf clips allow dark adaptation in the field; imaging fluorometers measure whole leaves or plants with LEDs; multiparametric fluorometers combine chlorophyll and flavonol signals, for example to detect nitrogen deficiency.

## Slide 12: Induction kinetics
What happens when a dark-adapted leaf is suddenly illuminated: the Kautsky effect, the OJIP rise and the slow PSMT phase
03
Notes: Historical and conceptual bridge: the induction curve was the first evidence that fluorescence tracks photosynthesis.

## Slide 13: The Kautsky effect (fluorescence induction)
Kautsky curve of a healthy green leaf: fast rise O → P (<1 s), then slow decay P → S → M → T over minutes
What you see
Dark-adapted leaf + continuous light
Fast phase (<1 s): exponential rise O → J → I → P
Slow phase (minutes): decline P → S → M → T to a steady state
What it means
Rise = PSII acceptors (QA, PQ pool) become reduced → centres close
Decline = quenching: Calvin cycle activation, stomatal opening and NPQ
Kautsky & Hirsch (1931) linked the decline to the onset of CO₂ assimilation
A true Kautsky effect is seen at moderate light (<200 µmol m⁻² s⁻¹); at high irradiance (≥500 µmol m⁻² s⁻¹) the trace looks like the stylised PAM trace in Module 05.
Notes: Kautsky and Hirsch (1931) watched dark-adapted leaves suddenly illuminated: fluorescence rose to a peak within about a second, then declined over minutes to a steady state. They noticed that the decline mirrored the start of CO2 assimilation. The fast rise reflects the filling up (reduction) of the electron acceptors of PSII; the slow decline reflects quenching as photosynthesis and NPQ switch on.

## Slide 14: Zooming into the fast rise: the OJIP transient
Chart: Idealised OJIP transient (log-spaced time axis; O, J, I, P marked on the axis)
| O 0.01 | 0.02 | 0.05 | 0.1 | 0.2 | 0.5 | 1 | J 2 | 5 | 10 | I 30 | 100 | P 300 | 1000
Fluorescence (relative) | 500 | 505 | 520 | 570 | 680 | 900 | 1150 | 1300 | 1380 | 1480 | 1700 | 2150 | 2400 | 2380
O
20–50 µs
Fo: all QA oxidised, centres open
J
~2 ms
QA⁻ accumulates (photochemical phase)
I
~30 ms
Plastoquinone pool partly reduced
P
~300 ms+
Fm: all QA reduced, centres closed
Interpretation follows the JIP-test convention (Strasser et al. 2004). Murchie & Lawson caution that complex OJIP-derived parameters still lack broad empirical support.
Notes: Plotting the first second on a logarithmic time axis reveals steps O, J, I and P. The common interpretation (JIP-test, Strasser et al. 2004): O is Fo with all QA oxidised; O to J is the photochemical phase where QA is reduced; J to I and I to P reflect progressive reduction of the plastoquinone pool and the PSI acceptor side. Many parameters are derived from these points, but the paper warns that the more complex ones lack strong empirical support.

## Slide 15: Fast phase vs slow phase (OJIP vs PSMT)
Measured OJIP rise on a log time axis (inset: the whole Kautsky curve)
Full induction: fast phase O-J-I-P (~1 s) then slow phase P-S-M-T (minutes)
Fast phase OJIP (<1 s)
Reduction of PSII acceptors; used for dark-adapted parameters such as Fo, Fm, Fv/Fm.
Slow phase PSMT (minutes)
Energy transduction, ATP synthesis, CO₂ fixation, state transitions, NPQ.
Notes: The fast phase OJIP (under a second) is about filling the electron acceptors of PSII. The slow phase PSMT (minutes) is about the rest of the plant metabolism catching up: ATP synthesis and energy transduction, Calvin cycle activation and CO2 fixation, state transitions and non-photochemical quenching. These slow changes are what quenching analysis with saturating pulses separates.

## Slide 16: PSII redox state & quenching
Open vs closed reaction centres, photochemical and non-photochemical quenching, and the saturating-pulse trick
04
Notes: This module explains the mechanism behind every PAM parameter.

## Slide 17: Open and closed PSII reaction centres
H₂O → OEC
P680
Pheo
QA
QB
PQ pool
Cyt b₆f
PSI → NADPH
e⁻ flow →
QA accepts only ONE electron at a time
QA
OPEN centre
QA oxidised — ready to accept an electron
Photochemistry possible
Fluorescence low (e.g. Fo in the dark)
Excitation energy is used
QA⁻
CLOSED centre
QA⁻ reduced — waiting to pass its electron to QB
No photochemistry until QA re-oxidises
Fluorescence high (e.g. Fm in a pulse)
Quantum efficiency of PSII declines
Light intensity and temperature (via metabolic state) set how many centres are closed at any moment. More closure → lower PSII quantum efficiency → higher fluorescence (unless NPQ rises too).
Notes: P680 ejects an electron (from water splitting) to pheophytin and then to QA, a bound quinone. QA can hold only one electron. Until QA passes it to QB, that reaction centre cannot do photochemistry: it is 'closed'. Closed centres cannot use excitation energy, so more of it leaves as fluorescence or heat. The fraction of closed centres depends on light intensity and on how fast downstream metabolism takes electrons away.

## Slide 18: Paper Figure 1: events in PSII behind the parameters
Murchie & Lawson (2013), Fig. 1 — (A) PSII electron transport, (B) Fo and Fm in a dark-adapted leaf, (C) open → closed centre
A
Excitation energy in LHCII goes to photochemistry, heat (NPQ) or fluorescence. Electrons: H₂O → OEC → P680 → Pheo → QA → QB → PQ.
B
Measuring beam on → Fo (centres open). Saturating pulse → Fm (centres closed). Fv = Fm − Fo.
C
P680 → P680∗ (excited) → P680⁺QA⁻ after charge separation. QA⁻ cannot accept another electron → closed centre.
Notes: Panel A shows the PSII complex: LHCII antenna feeding CP43/CP47, the D1/D2 core with P680, pheophytin, QA and QB, and the oxygen-evolving complex. Panel B shows a dark-adapted trace: the measuring beam gives Fo (centres open), a saturating pulse gives Fm (centres closed), and their difference is Fv. Panel C shows the sequence that turns an open centre into a closed one.

## Slide 19: What is 'quenching'?
Dark-adapted vs light-adapted traces: Fm′ < Fm because of non-photochemical quenching; Ft (F′) < Fm′ because of photochemical quenching
① Photochemical quenching (qP)
Light activates Calvin-cycle enzymes; metabolite pools in stroma and cytosol increase
Stomata open → more CO₂ for Rubisco (stomata respond ~10× slower than photosynthesis)
More electron sinks → QA re-oxidised → centres re-open
② Non-photochemical quenching (NPQ)
Rapid rise in the rate constant of heat dissipation on illumination
Photoprotective: removes excess excitation, prevents damaging free radicals
Competes with both fluorescence and photochemistry
Takes several minutes or longer from darkness; varies with species and environment.
Notes: After the initial rise under actinic light, fluorescence declines over minutes. Anything that lowers fluorescence is called quenching. Two families exist. Photochemical quenching: photosynthesis itself switches on (Calvin cycle enzymes activated, metabolite pools build up, stomata open) so electrons are drained and centres re-open. Non-photochemical quenching: the rate constant for heat dissipation increases.

## Slide 20: How NPQ is switched on: the molecular mechanism
Excess light
Linear + cyclic e⁻ flow pump H⁺ into lumen
Lumen acidifies: ΔpH builds up
PsbS protein
becomes protonated
VDE activated:
violaxanthin → zeaxanthin
Conformational change in PSII antenna →
excitation dissipated as heat (qE)
Key facts
Regulated by acidification of the lumen (ΔpH)
Needs PsbS and the xanthophyll cycle
Xanthophylls are carotenoids
A 'safe' valve: competes with photochemistry and fluorescence
Lowers Fm′ below Fm — the basis of the NPQ parameter
Notes: Trace the chain: excess light drives linear and cyclic electron flow, which pumps protons into the thylakoid lumen. The resulting ΔpH (acid lumen) does two things: it protonates the PsbS protein and it activates violaxanthin de-epoxidase, which converts violaxanthin to zeaxanthin. Both cause conformational changes in the PSII antenna that let it dump excitation energy as heat. This energy-dependent quenching is called qE.

## Slide 21: The xanthophyll cycle in detail
Violaxanthin
2 epoxides
Antheraxanthin
1 epoxide
Zeaxanthin
0 epoxides · quencher
VDE: high light · acidic lumen (low pH) · ascorbate →
← ZE: low light / darkness
Fast & reversible
Zeaxanthin + protonated PsbS give rapid qE that relaxes in seconds–minutes in the dark.
Sustained
Retained zeaxanthin (e.g. over-wintering evergreens) keeps quenching on and lowers Fv/Fm.
Optical signature
De-epoxidation changes reflectance at ~531 nm — the basis of the PRI index used with SIF.
Notes: In excess light the lumen becomes acidic and violaxanthin de-epoxidase (VDE) removes epoxide groups: violaxanthin to antheraxanthin to zeaxanthin. Zeaxanthin promotes heat dissipation in the antenna. In low light or darkness zeaxanthin epoxidase (ZE) reverses the reactions. Retained zeaxanthin causes long-lived (sustained) quenching. A second cycle, the lutein-epoxide cycle, occurs in some shade-tolerant or woody species.

## Slide 22: The saturating-pulse principle
Before the pulse (steady light)
open
closed
open
open
closed
open
closed
open
open
closed
open
closed
Some centres open, some closed → level F′
During the saturating pulse
closed
closed
closed
closed
closed
closed
closed
closed
closed
closed
closed
closed
All centres closed → qP = 0 → level Fm′ (or Fm if dark-adapted)
Pulse properties
Very bright (typically ~0.8 s at ≥4000 µmol m⁻² s⁻¹), shorter than 1 s so it does not change the leaf's state.
What it separates
Fq′ = Fm′ − F′ is the photochemical part; Fm − Fm′ reflects NPQ.
Old method
Herbicides (e.g. DCMU) blocking QB removed photochemistry — not practical routinely.
Notes: Herbicides that block QB were once used to remove photochemical quenching, which is impractical. Instead, a brief (<1 s), very bright flash temporarily closes every PSII centre. During the flash photochemical quenching is effectively zero and only non-photochemical processes remain. So the fluorescence measured during the pulse (Fm or Fm′) is the level the leaf would have with no photochemistry; the gap between that and the level just before the pulse is the photochemical part.

## Slide 23: PAM protocol & parameters
Reading a fluorescence trace: every level, every ratio, and a fully worked numerical example
05
Notes: Everything here comes from comparing fluorescence levels in darkness, under actinic light, and during saturating pulses.

## Slide 24: The typical PAM trace, step by step
Murchie & Lawson (2013), Fig. 2 — stylised trace of a dark-adapted leaf exposed to actinic light, darkness and saturating pulses
1
Measuring beam on (dark)
Minimum fluorescence Fo — all centres open, no NPQ
2
Saturating pulse (dark)
Maximum Fm — all centres closed; Fv = Fm − Fo
3
Actinic light on
Rise, then quenching to steady state F′ (minutes to >20 min)
4
Pulses in the light
Fm′ < Fm because of NPQ; Fq′ = Fm′ − F′
5
Actinic off (+ far-red)
Minimal level in light-adapted state Fo′; Fv′ = Fm′ − Fo′
6
Pulses in the dark
Fm′ recovers towards Fm as NPQ relaxes (20–30 min)
Notes: Follow the numbers on the right with the trace. Steps 1 to 2 are the dark-adapted measurement, 3 to 4 the light-adapted measurement, and 5 to 6 the dark relaxation used to study NPQ components. This stylised trace corresponds to an induction at high irradiance (≥500 µmol m-2 s-1).

## Slide 25: Glossary of fluorescence levels
Fo
DARK
Minimal fluorescence, dark-adapted
All PSII centres open, no NPQ
Fm
DARK
Maximal fluorescence, dark-adapted
Saturating pulse closes all centres; no NPQ
Fv
DARK
Variable fluorescence
Fv = Fm − Fo
F′ (Fs, Ft)
LIGHT
Steady-state fluorescence in light
Some centres closed, NPQ present
Fm′
LIGHT
Maximal fluorescence in light
Pulse under actinic light; lowered by NPQ
Fo′
LIGHT
Minimal fluorescence in light
Just after actinic off (+FR) or calculated
Fq′
LIGHT
Photochemical quenching by open centres
Fq′ = Fm′ − F′
Fv′
LIGHT
Variable fluorescence in light
Fv′ = Fm′ − Fo′
Notes: These eight symbols are the building blocks for every ratio. Keep one rule in mind: a prime (′) means the leaf is light-adapted; no prime means dark-adapted.

## Slide 26: Fv/Fm: maximum quantum efficiency of PSII
~0.83
typical Fv/Fm of an unstressed leaf
Fv/Fm = (Fm − Fo) / Fm
Reading the value (dark-adapted leaf)
< 0.6: severe PSII damage
0.6–0.78: photoinhibition / sustained quenching
≈ 0.8–0.83: healthy
0.5
0.6
0.7
0.8
Scale starts at 0.5. Zone limits are approximate; compare with non-stressed controls of the same species.
How to measure
Dark-adapt ≥20 min (leaf clip)
Check zero; set measuring beam so it causes no rise
Measure Fo, then a saturating pulse → Fm
Pre-dawn values for long-term stress
What lowers it
Photoinhibition: inactivation/damage of PSII (D1 protein)
Sustained quenching (e.g. retained zeaxanthin, drought, winter)
Rise in Fo → damage; fall in Fm → quenching
Meaning
Correlates with the maximum quantum yield of photosynthesis (O₂ or CO₂ per photon) at limiting light.
Notes: Fv/Fm is the fraction of absorbed light that PSII could use for photochemistry if every centre were open and there were no NPQ. It is measured on fully dark-adapted leaves. In unstressed leaves it is remarkably constant, around 0.83. A drop means PSII damage (photoinhibition) or sustained quenching. Because it is so easy, it is the most common 'stress' measurement, but see the pitfalls in Module 06.

## Slide 27: ΦPSII = Fq′/Fm′: PSII operating efficiency
ΦPSII = Fq′ / Fm′ = (Fm′ − F′) / Fm′
also written ΔF/Fm′ · Y(II) · 'yield'
Decomposition
Fq′/Fm′
operating efficiency
=
Fq′/Fv′ (qP)
fraction of centres open
×
Fv′/Fm′
max efficiency in light
↓ Fv′/Fm′ means NPQ ↑
Electron transport rate (ETR)
ETR = ΦPSII × PAR × 0.84 × 0.5
0.84 = typical leaf absorptance; 0.5 = share of light to PSII (both are assumptions)
Why it is popular — and the catch
No dark adaptation needed; quick in the field
Strongly depends on current PAR — always record light at the leaf surface
Notes: PhiPSII is the fraction of absorbed light actually used by PSII photochemistry right now, under the current light. It needs no dark adaptation, which is why it is the most used light parameter. It factorises into two terms: how many centres are open (qP) times how efficient an open centre is given the current NPQ (Fv′/Fm′). Multiply by absorbed light to get the electron transport rate.

## Slide 28: qP and qL: how many PSII centres are open?
qP — photochemical quenching
qP = Fq′/Fv′ = (Fm′ − F′)/(Fm′ − Fo′)
Proportion of PSII centres that are open (approx.)
1 − qP ≈ closed centres (excitation pressure)
Non-linear with true open fraction — use with care
qL — the 'lake model' version
qL = (Fq′/Fv′) × (Fo′/F′) = qP × Fo′/F′
Estimates the fraction of open PSII centres
Accounts for energy sharing between connected PSII units
Considered a more accurate redox-state indicator
Picture it: 10 PSII centres under actinic light
6 open (green) · 4 closed (red) → qL ≈ 0.6 ; 1 − qL ≈ 0.4
Use cases
Onset of photoinhibition
Level of photoprotective quenching
Requires Fo′ (measured with FR or calculated)
qP and qL are both 1 when all centres are open; they differ in between because of antenna connectivity.
Notes: qP compares the photochemical part of the light-adapted variable fluorescence to its maximum, so it approximates the fraction of open centres. 1 − qP approximates the closed fraction and has been used as an indicator of excitation pressure and photoinhibition onset. The relation with open centres is not linear because PSII units share antennae (connectivity), so qL, which adds the correction Fo′/F′, is considered a better indicator of the redox state of QA.

## Slide 29: NPQ: non-photochemical quenching
NPQ = (Fm − Fm′) / Fm′
Meaning
Estimates the rate constant for heat loss from PSII
0 in a fully dark-adapted leaf; typically rises to ~1–3+ in high light
Caution
Needs a true Fm: if dark-adapted Fv/Fm is well below 0.83, treat NPQ with caution
Photoinhibited leaves have lower Fm → NPQ underestimated → don't compare across different Fv/Fm
Classic notation: Y = (Fm′−F)/Fm′, qP = (Fm′−F)/(Fm′−Fo′), qN = 1 − (Fm′−Fo′)/(Fm−Fo); ML, SP, AL, FR markers
Notes: NPQ (Stern–Volmer form) estimates the rate constant of heat loss from PSII relative to the dark-adapted state. It compares Fm in the dark with Fm′ in the light, so it is the only parameter that needs dark-adapted values. Danger: if a leaf is already photoinhibited, its Fm is lower, so NPQ appears lower even when heat dissipation is high. Do not compare NPQ between leaves whose Fv/Fm values differ. Older literature used qN = 1 − Fv′/Fv.

## Slide 30: Summary table of commonly used parameters
Parameter | Also known as | Formula | Description | Needs
Fv/Fm | — | (Fm − Fo)/Fm | Maximum quantum efficiency of PSII photochemistry | dark
Fv′/Fm′ | — | (Fm′ − Fo′)/Fm′ | Maximum efficiency of PSII in the light, if all centres were open | Fo′
Fq′/Fm′ | ΦPSII, ΔF/Fm′, Y(II) | (Fm′ − F′)/Fm′ | PSII operating efficiency: quantum efficiency of PSII electron transport in the light | —
Fq′/Fv′ | qP | (Fm′ − F′)/(Fm′ − Fo′) | Photochemical quenching; non-linear with fraction of open centres (see qL) | Fo′
NPQ | — | (Fm − Fm′)/Fm′ | Non-photochemical quenching: rate constant for heat loss from PSII | dark
qL | — | (Fq′/Fv′)(Fo′/F′) | Estimates the fraction of open PSII centres | Fo′
'Needs': dark = requires dark-adapted Fo/Fm; Fo′ = requires measured (far-red) or calculated Fo′.
Notes: This is Table 1 of Murchie & Lawson (2013). Notice which parameters need a dark-adapted measurement (Fv/Fm, NPQ) and which need Fo′ (Fv′/Fm′, qP, qL). PhiPSII needs neither, which explains its popularity.

## Slide 31: Worked example: calculate every parameter
Readings from one leaf (arbitrary units)
Fo
200
Fm
1000
F′
400
Fm′
600
Fo′
180
PAR
1000
Dark (navy) · light-adapted (amber). PAR in µmol m⁻² s⁻¹.
Parameter | Calculation | Result | Meaning
Fv/Fm | (1000 − 200)/1000 | 0.80 | Healthy PSII
Fv′/Fm′ | (600 − 180)/600 | 0.70 | Max efficiency in light (NPQ lowers it)
ΦPSII | (600 − 400)/600 | 0.33 | ⅓ of absorbed light used by PSII
qP | (600 − 400)/(600 − 180) | 0.48 | ≈ half of centres open
Check | qP × Fv′/Fm′ = 0.476 × 0.70 | 0.33 | = ΦPSII ✓
qL | 0.476 × 180/400 | 0.21 | Lake-model open fraction
NPQ | (1000 − 600)/600 | 0.67 | Moderate heat dissipation
ETR | 0.333 × 1000 × 0.84 × 0.5 | 140 | µmol e⁻ m⁻² s⁻¹
Fo′ calc. | 200/(0.80 + 200/600) | 176 | vs 180 measured ✓
Notes: Use these made-up but realistic readings to check you can compute everything by hand. Notice the internal consistency: PhiPSII equals qP times Fv′/Fm′, and the calculated Fo′ (Oxborough & Baker) is close to the measured one. Interpretation: PSII is healthy (0.80), one third of absorbed light is used photochemically at this light, about half the centres are open by qP, and NPQ is moderate.

## Slide 32: Good practice & pitfalls
How long to dark-adapt, what Fv/Fm can and cannot tell you, problems in the light, and the link to CO₂ assimilation
06
Notes: Most mistakes in fluorescence work are interpretation mistakes, not instrument mistakes.

## Slide 33: To dark-adapt or not? The components of NPQ
seconds
minutes
~30 min
hours
days
qE · ΔpH, PsbS, zeaxanthin
qT · state transitions
qI · photoinhibition, D1 repair, retained zeaxanthin
Relaxation time in darkness
NPQ relaxation after actinic light off: qE (fast), qT and qI (slow) separate
Practical rule
20–30 min dark usually removes qE and qT for a plant in a moderate environment.
Best answer
Test it: dark-adapt non-stressed controls and measure Fv/Fm every 5–10 min until stable.
Long-term stress
Use pre-dawn Fv/Fm (e.g. drought, over-wintering evergreens).
Notes: NPQ is not one process. qE, energy-dependent quenching, relaxes within seconds to minutes once ΔpH collapses. qT, state transitions, moves LHCII between PSII and PSI over minutes and matters mostly in low light. qI, photoinhibitory or sustained quenching, relaxes slowly over hours or longer; it includes D1 damage and repair and long-lived zeaxanthin. So the dark adaptation time decides which components you have removed. For a plant adapted to its environment, 20-30 min usually removes qE and qT; whatever remains is qI.

## Slide 34: Pitfalls in measuring Fo and Fm
Measuring beam too strong
Induces electron transport → false (high) Fo. Lower intensity / frequency if Fo drifts up.
QA partly reduced in the dark
Chlororespiration reduces PQ. Use a far-red pulse to oxidise QA before Fo.
NPQ not fully relaxed
Zeaxanthin quenching relaxes slowly → Fm underestimated. Dark-adapt long enough.
Pulse not saturating
~2000 µmol m⁻² s⁻¹ may miss true Fm′ in high light; aim 4000–8000 (more for C₄).
High modulation frequency in the dark
Useful during pulses but not for Fo; most devices switch automatically.
Quenching during the pulse
Check there is no decline during the pulse (pulse too long).
Notes: Fo can be falsely high if the measuring beam is too strong or modulated too fast, because it then drives some charge separation; check that switching on the beam causes no rise. QA can also be partly reduced in the dark by chlororespiration; a far-red pulse before Fo oxidises it. For Fm the pulse must be truly saturating: about 2000 µmol m-2 s-1 is probably enough for dark-adapted Fm but often not for Fm′ under high actinic light; most instruments give 4000-8000, and C4 plants may need more.

## Slide 35: Interpreting Fv/Fm: four common misconceptions
(i) Cause is hard to assign
Leaf optical properties change under stress (e.g. drought) → Fm and Fo change via absorptance. The ratio removes this, but its cause still needs other data.
(ii) Lower Fv/Fm ≠ lower photosynthesis
Fv/Fm relates to the light-limited quantum yield. A leaf can have reduced Fv/Fm with no penalty at high, saturating light.
(iii) Stress may need high light to show
Inactivation of PSII may only appear when light is high enough; otherwise no difference between treatments.
(iv) It only sees PSII
Stress elsewhere (e.g. roots) may not change Fv/Fm. Fluorescence is not a generic stress detector.
Imaging Fv/Fm of plants
Takeaway
Use Fv/Fm with light-adapted data, controls and other measurements.
Notes: These four points from the review prevent the classic over-interpretation that any drop in Fv/Fm means the plant is photosynthesising less, or that fluorescence is a generic plant stress detector.

## Slide 36: Problems with measurements in the light
ΦPSII depends on light
Varies substantially with even small PAR changes
Record PAR at the leaf surface, or measure when PAR is saturating
Ensure steady state (F′ stable) before the pulse
ETR assumptions
Absorptance 0.84 and PSII share 0.5 are averages, not constants
Don't compare ETR of drought-stressed (low turgor) vs hydrated leaves
Pigment content and PSII:PSI stoichiometry change these values
Errors in Fo′ → calculate it
Fo′ = Fo / [ (Fv/Fm) + (Fo/Fm′) ]
Oxborough & Baker (1997). Valid if: PSII centres open at Fo; no change in down-regulation between Fo/Fm; no change in photoinhibition between Fm′ and Fm.
Other small errors
PSI fluorescence above 700 nm adds to the signal
Multiple turnovers of PSII during the pulse
Mostly minor: ΦPSII agrees well with quantum yield of CO₂ assimilation
Notes: PhiPSII depends strongly on the current light, so PAR at the leaf surface must be measured. Converting PhiPSII to ETR assumes absorptance 0.84 and equal light sharing between PSII and PSI; these break down for drought-stressed leaves, leaves with different pigment content or acclimation state. Fo′ can be wrong if the far-red light does not fully oxidise QA or if NPQ relaxes quickly after actinic off; then calculate Fo′ instead with the Oxborough & Baker equation. PSI contributes to fluorescence above 700 nm and multiple turnovers during the pulse add small errors.

## Slide 37: Linking fluorescence to CO₂ assimilation
PSII electron
transport (ETR)
CO₂ assimilation (Calvin cycle)
~4 e⁻ per CO₂ when photorespiration is blocked
Photorespiration (C₃)
Rises with stomatal closure, heat
Mehler reaction / cyclic flow
Alternative sinks under stress
Implication
Linear Fq′/Fm′ ↔ CO₂ uptake only holds when the allocation of electrons is constant — hard to guarantee in the field.
C₃ vs C₄
C₃: close correlation at 2 % O₂; photorespiration breaks linearity
C₄: CO₂-concentrating mechanism suppresses photorespiration → more linear
Measuring PSI too
P700 redox via near-infrared absorbance (810–840 nm)
Combine ΦPSI with ΦPSII; cyclic flow affects ΔpH and NPQ
PSII:PSI ETR ratios need stoichiometry corrections
Notes: ATP and NADPH from linear electron transport are used in carbon fixation in fixed ratios, so PhiPSII and the quantum yield of CO2 fixation correlate. In C3 plants the link is cleanest when photorespiration is suppressed (2% O2): then about 4 electrons are needed per CO2. Photorespiration, the Mehler reaction and cyclic electron flow are alternative electron sinks that change the ratio, for example during stomatal closure, temperature change or stress. In C4 plants the CO2-concentrating mechanism suppresses photorespiration, so the relation is more linear. PSI redox (P700 absorbance at 810–840 nm) can be measured alongside.

## Slide 38: Standard measurement protocols (A, B, C)
A · Fv/Fm
1
Dark-adapt ≥20 min (leaf clip); keep dark throughout
2
Detector on, measuring beam off: check zero
3
Beam on: check it causes no rise; adjust
4
Measure Fo
5
Saturating pulse ~0.8 s at ≥4000 µmol m⁻² s⁻¹ → Fm
6
Check no quenching during pulse
7
Non-stressed control should give 0.81–0.83
B · ΦPSII and NPQ
1
Follow A, then switch on actinic light
2
Wait for steady state (minutes); record PAR
3
If ambient light: wait until F′ is stable
4
Apply saturating pulse → Fm′
5
NPQ needs dark-adapted Fm from A
6
Calculate using Table 1
C · qP (Fq′/Fv′)
1
As B, but Fo′ is also needed
2
After the pulse switch actinic off
3
Measure Fo′ after a few seconds
4
Use far-red to oxidise PSI, QA and carriers
5
Or calculate Fo′ from Fo (Oxborough & Baker)
Notes: These are the three protocols given at the end of the review. Most devices calculate the values automatically; the careful user should check these steps and compare results with the stylised trace.

## Slide 39: Imaging, applications & monitoring
From single-spot measurements to images, screening platforms and remote, long-term monitoring
07
Notes: Imaging uses the same principles but over an area, which reveals heterogeneity a point measurement would miss.

## Slide 40: Chlorophyll fluorescence imaging
Advantages
Spatial heterogeneity within leaves/plants
Screening many plants under identical conditions
Resolution from chloroplasts and guard cells to whole plants
Combined techniques
+ IRGA gas exchange: CO₂ diffusion, guard-cell photosynthesis
+ thermography: stomatal behaviour, water-use efficiency
+ hyperspectral: disease detection (e.g. head blight)
Requirements
Leaf flat, horizontal, at correct height
Even actinic illumination over the area
Pulse saturating everywhere (4000–8000 µmol m⁻² s⁻¹)
Limitations
Costlier; large LED banks; mostly lab-based
Often no FR source → Fo′ is calculated
Field versions: e.g. Imaging-PAM MINI, FluorCam, rover systems
Pixel-to-pixel image arithmetic: measured F₀, Fm, Fs, Fm′ → calculated Fv/Fm, ΦPSII, NPQ maps
Notes: Imaging systems use banks of LEDs for measuring, actinic and saturating light and a camera instead of a fibre-optic probe. Each pixel gets its own Fv/Fm, PhiPSII or NPQ. This reveals spatial heterogeneity (e.g. patchy stomatal closure, infection sites), lets many plants be screened at once under identical conditions, and can be combined with gas exchange, thermography or hyperspectral sensors.

## Slide 41: Paper Figure 3: what imaging can reveal
a · b
Steady-state F′ and ΦPSII of a leaf in a chamber: patchy stomatal closure after humidity drop
c
Herbicide screening of Arabidopsis seedlings in a 96-well plate (Fv/Fm)
d
ΦPSII heterogeneity of Arabidopsis after high light
e
Fv/Fm of guard-cell chloroplasts (high-resolution microscope)
f
Screening transgenic plants with reduced SBPase
g
Fv/Fm of wheat varieties: rust susceptibility
h
ΦPSII decline as DCMU travels in via the petiole
i
Cadmium effect on ΦPSII in Lemna
Notes: (a, b) steady-state fluorescence and PhiPSII showing patchy stomatal closure after a humidity drop; (c) herbicide screening of Arabidopsis in a 96-well plate; (d) heterogeneity in PhiPSII of two Arabidopsis plants; (e) guard-cell chloroplasts in Tradescantia epidermis at high resolution; (f) transgenic plants with reduced SBPase; (g) wheat varieties with different rust susceptibility; (h) DCMU uptake via the petiole; (i) cadmium effects in the aquatic plant Lemna.

## Slide 42: Imaging applications: fruit, development and cyanobacteria
Post-harvest lemon damage: F₀, Fs, Fm and Fv/Fm images reveal damaged areas
Green mould infection of lemons over 0–84 h
Leaf development: young vs old leaf images and kinetics
Heterocysts (arrows) in cyanobacteria are dark in Fm fluorescence
Notes: These examples from the original slides show how Fm and other images reveal damage before it is visible: post-harvest damage and green mould infection of lemons appear in fluorescence images, young and old leaves differ in their kinetics, and heterocysts in cyanobacteria (which do not have PSII activity) appear dark in Fm images.

## Slide 43: Stress phenotyping example: cadmium and salt
Fv/Fm, YII and NPQ images and time courses under Cd, NaCl and Cd+NaCl stress
How to read it
Rows: Fv/Fm, Y(II), NPQ
Columns: Control, Cd, Na, Cd+Na at 2 and 3 weeks
Colour scale: blue/purple = high, yellow/red = low
Lessons
Parameters respond differently and over different times
Images show where in the leaf damage starts
Combine dark (Fv/Fm) and light (Y(II), NPQ) parameters
Notes: Images of Fv/Fm, Y(II) (= PhiPSII) and NPQ of leaves under control, cadmium, NaCl and combined stress after 2 and 3 weeks, with the corresponding time courses below. Note that each parameter responds differently and with a different time course, which is why measuring several parameters is more informative than Fv/Fm alone.

## Slide 44: Towards long-term and remote monitoring
Leaf clip PAM
mm–cm · seconds
Monitoring PAM
fixed heads · weeks–seasons
LIFT (laser)
5–50 m · canopy, active
UAV / airborne
m · passive SIF
Satellite
300 m–km · passive SIF
ACTIVE (instrument supplies the light)
PASSIVE (sunlight only) →
Monitoring PAM
Modular heads measure F′ and, with pulses, Fm′; used for annual NPQ in boreal forest and rice canopies.
LIFT
Laser projects a ~100 mm spot onto the canopy; telescope + photodiode give PSII yield and electron transport at 5–50 m.
Passive sensing
No saturating pulse and uneven illumination, but continuous, large-area coverage → SIF.
Notes: Field physiologists need to link second-scale measurements to growth over weeks and months. Monitoring PAM systems leave measuring heads clipped on leaves for weeks, powered by solar panels; at night Fm′ and Fo′ become Fm and Fo. LIFT uses a laser to excite canopies from 5–50 m and measures PSII yield remotely. Beyond that, no artificial light can saturate a canopy, so we switch to passive sensing of sunlight-induced fluorescence in Fraunhofer lines and oxygen bands: this is SIF.

## Slide 45: Sun-induced fluorescence (SIF)
Measuring the same red glow passively under sunlight — from leaf to satellite. Based on Mohammed et al. (2019), '50 years of progress'
08
Notes: SIF uses the sun as the excitation source and exploits dark absorption lines in the solar spectrum to separate a tiny fluorescence signal from reflected light.

## Slide 46: Active (PAM) vs passive (SIF) fluorescence
 | Active — PAM fluorometry | Passive — SIF
Light source | Instrument (ML, AL, SP, FR) | The sun
Saturating pulse | Yes → Fm, Fm′ | No
What it gives | Yields and ratios (Fv/Fm, ΦPSII, NPQ) | Absolute flux (mW m⁻² sr⁻¹ nm⁻¹)
Scale | Leaf, single plants (cm–m) | Leaf to globe (m–km)
Spectral bands | Usually one broad band >700 nm | Red (~687) and far-red (~760) bands or full 650–800 nm
Main challenge | Protocol, dark adaptation | Signal is ~1–5 % of reflected radiance; atmosphere; canopy structure
Typical use | Plant physiology, phenotyping | GPP, stress mapping, ecosystem monitoring
Notes: The physics is the same, but the measurement is completely different. PAM controls the light and uses saturating pulses to obtain yields. SIF cannot control the light: it measures the absolute fluorescence flux emitted under ambient sunlight, which depends on how much light is absorbed (APAR), the fluorescence yield, and how much escapes the canopy.

## Slide 47: A short history of SIF
1834
Brewster: red light from laurel leaf extract
1852
Stokes coins 'fluorescence'
1874
Müller: link to assimilation
1931
Kautsky & Hirsch: induction kinetics
1940
McAlister & Myers: two processes vs CO₂
1963
Duysens & Sweers: modulated light, NPQ concept
1975
Plascyk: Fraunhofer Line Discriminator (FLD)
1986
Schreiber: PAM fluorometer
2000
Zarco-Tejada: SIF in canopy reflectance
2011
GOSAT: first global SIF maps
2015
ESA selects FLEX (8th Earth Explorer)
2017
TROPOMI (Sentinel-5P) launched
Active, leaf-level science
Passive, remote sensing
Notes: Fluorescence was first seen in 1834 by Brewster in a laurel extract. Stokes coined the word in 1852; Müller in 1874 suggested a link with assimilation; Kautsky and Hirsch in 1931 established it. McAlister and Myers showed both inverse and direct relationships with CO2 uptake; Duysens and Sweers pioneered modulated light and described what we now call NPQ. Plascyk's Fraunhofer Line Discriminator (1975) and Schreiber's PAM (1986) followed. Around 2000 Zarco-Tejada demonstrated fluorescence in canopy reflectance; in 2011 GOSAT gave the first global SIF maps; FLEX was selected by ESA in 2015, and TROPOMI launched in 2017.

## Slide 48: The SIF emission spectrum
Mohammed et al. (2019), Fig. 1 — energy partitioning and the leaf fluorescence spectrum (PSII + PSI contributions)
Red peak F685
~685–690 nm
Mostly PSII
Strongly re-absorbed by chlorophyll
Far-red peak F740
~730–740 nm
PSII + PSI
Escapes the canopy more easily
Key numbers & terms
Fluorescence quantum yield in vivo <10 %, typically 0.5–3 %
Steady-state fluorescence (Fs, Ft) is what SIF measures under sunlight
Thermal dissipation: constitutive (basal) + regulated (NPQ, xanthophyll cycle)
Units: mW m⁻² sr⁻¹ nm⁻¹ (radiance)
Notes: In an intact leaf, fluorescence spans about 650–800 nm with two peaks: red near 685–690 nm (F685) and far-red near 730–740 nm (F740). PSII emits in both regions; PSI mainly in the far-red. In healthy green leaves the red peak is lower than the far-red peak because chlorophyll re-absorbs red fluorescence on its way out of the leaf. The same figure also restates the three fates of absorbed energy.

## Slide 49: Re-absorption and scattering: leaf to canopy
Mohammed et al. (2019), Fig. 7 — SCOPE: (a) reflectance, (b) escape probability f_esc, (c) emitted fluorescence, (d) top-of-canopy SIF for Cab 5–80 µg cm⁻²
Leaf level
Red emission overlaps chlorophyll absorption → re-absorbed
Red/far-red ratio ↓ as chlorophyll ↑
Canopy level
Escape probability fesc ≈ shape of reflectance
LAI, leaf angle, clumping, sun/shade leaves change SIF
Only a little red SIF leaves the shaded side of leaves
Consequence: a change in SIF may come from physiology or from structure and pigments — models are needed to tell them apart.
Notes: Chlorophyll absorbs between ~400 and 720 nm, overlapping the red emission, so red fluorescence is re-absorbed inside the leaf and canopy, and saturates quickly as chlorophyll increases. Far-red escapes much more. Therefore the red/far-red ratio falls as chlorophyll content rises (Gitelson's F735/F700 index). In the canopy, scattering and re-absorption shape the observed SIF: the fluorescence escape probability fesc looks very similar to reflectance. The SCOPE simulation shows this for four leaf chlorophyll contents.

## Slide 50: The core difficulty: SIF is tiny compared with reflected light
Mohammed et al. (2019), Fig. 8 — SIF (red, right axis %) vs total radiance (grey) at 0.1 nm; insets: O₂-B (left) and O₂-A (right)
~1–5 %
of total radiance outside absorption bands
>10 %
inside the O₂-A and O₂-B bands
Why the bands help
Inside a band the sun's light is strongly attenuated → reflected radiance is low
Fluorescence is emitted at all wavelengths → it fills in the band
Red: SIF fraction high (reflectance is low) despite re-absorption
Needs high spectral resolution (sub-nm) and high SNR
1–5 % is an approximate range for the overall contribution.
Notes: Plotted at 0.1 nm resolution for dense summer vegetation, top-of-canopy radiance (grey) is dominated by reflected sunlight; SIF (red) is only a few per cent of it overall. But inside narrow absorption bands where incoming sunlight is very dim, the relative contribution of SIF jumps: more than 10% in the O2-A (760 nm) and O2-B (687 nm) bands. That is the trick every retrieval method uses.

## Slide 51: Where to look: Fraunhofer lines and oxygen bands
Mohammed et al. (2019), Fig. 4 — olive canopy radiance showing O₂-B and O₂-A (left) and the O₂-A band in detail (right)
Feature | Wavelength | Origin | Used for
Hα | 656.3 nm | Fraunhofer line | Early FLD work (narrow, ~0.1 nm)
O₂-B | ~687 nm | Telluric (Earth O₂) | Red SIF
Fraunhofer lines | 745–758 nm, K I 770 nm | Solar atmosphere | Far-red SIF from satellites
O₂-A | ~760 nm | Telluric (Earth O₂) | Far-red SIF; deepest band
Fraunhofer lines (solar)
Narrow; small in-filling signal
Earth's atmosphere does not change relative depth → simpler correction
Used by GOSAT, GOME-2, OCO-2, TROPOMI
O₂ bands (telluric)
Wide and deep → strong in-filling
Depth depends on path length, pressure, aerosols, direct/diffuse light
Needs accurate atmospheric modelling (FLEX design)
Notes: Two kinds of dark lines exist in the sunlight reaching vegetation. Fraunhofer lines are produced by gases in the sun's own atmosphere; they are narrow and fairly shallow, but the Earth's atmosphere hardly affects their relative depth, so atmospheric modelling is easier, which is why satellites use them. Telluric oxygen bands are produced by O2 in Earth's atmosphere; they are wide and deep, giving a strong in-filling signal, but they require accurate atmospheric correction.

## Slide 52: The retrieval equation and the FLD principle
L(λ) = r(λ)·E(λ)/π + SIF(λ)
L = radiance at sensor · E = incident irradiance · r = reflectance
Chart: In-filling of the O₂-A band by fluorescence (schematic)
| 755.0 | 755.5 | 756.0 | 756.5 | 757.0 | 757.5 | 758.0 | 758.5 | 759.0 | 759.5 | 760.0 | 760.5 | 761.0 | 761.5 | 762.0 | 762.5 | 763.0 | 763.5 | 764.0 | 764.5 | 765.0
Irradiance E (normalised) | 1 | 1 | 1 | 1 | 1 | 0.998 | 0.989 | 0.947 | 0.822 | 0.576 | 0.285 | 0.15 | 0.285 | 0.576 | 0.822 | 0.947 | 0.989 | 0.998 | 1 | 1 | 1
Canopy radiance L (normalised) | 1 | 1 | 1 | 1 | 1 | 0.999 | 0.99 | 0.952 | 0.838 | 0.614 | 0.35 | 0.227 | 0.35 | 0.614 | 0.838 | 0.952 | 0.99 | 0.999 | 1 | 1 | 1
Two-band FLD solution
Inside band: Lin = r·Ein/π + F
Outside band: Lout = r·Eout/π + F
F = (Eout·Lin − Ein·Lout) / (Eout − Ein)
Assumption to remember
r and F are constant across the narrow window — refined by 3FLD, iFLD, cFLD and spectral fitting.
Notes: Top-of-canopy radiance is the sum of reflected sunlight and fluorescence. With two unknowns (r and SIF) at each wavelength we need two measurements: one inside the absorption band and one just outside. If r and SIF are assumed equal at both, we can solve for SIF. The chart shows the idea: normalised to the shoulder, the radiance dip is shallower than the irradiance dip, because fluorescence fills it in. 3FLD, iFLD and cFLD improve on the constant-r/F assumption.

## Slide 53: Families of SIF retrieval methods
SIF retrieval methods
① Selected absorption bands
② Full SIF spectrum (650–800 nm)
O₂ bands
FLD (Plascyk 1975)
3FLD, iFLD, cFLD (refined r, F shapes)
SFM spectral fitting over tens of nm
Fraunhofer lines
Physically based (Frankenberg 2011)
Data-driven PCA / SVD (Guanter, Joiner, Köhler)
Used by satellites (GOSAT, GOME-2, OCO-2, TROPOMI)
Spectrum fitting
FSR, aFSR (basis spectra from SCOPE)
F-SFM full-spectrum fitting
SpecFit (piecewise cubic spline)
Model inversion
Invert canopy RTM (SCOPE) at TOA/TOC
Verhoef 2018 (FLEX + Sentinel-3)
Celesti 2018 · also gives Cab, LAI, fAPAR
Notes: Table 2 of the review groups methods into two classes. Class one retrieves SIF only at selected absorption bands: either O2 bands (FLD and variants, spectral fitting methods SFM) or Fraunhofer lines (simple physically based fitting, or data-driven PCA/SVD approaches using non-vegetated reference pixels). Class two retrieves the full SIF spectrum: spectrum fitting with basis spectra (FSR, F-SFM, SpecFit) or inversion of a canopy radiative transfer model, which also returns parameters like chlorophyll, LAI and fAPAR.

## Slide 54: Atmosphere, illumination and observation: the confounders
Atmospheric correction
O₂ bands need accurate RT (MODTRAN, T-18 system); one-step vs two-step schemes
Direct vs diffuse light
Diffuse light travels a longer path → deeper band → SIF over/under-estimated (up to 20 % at O₂-A)
Anisotropy & geometry
Sun/view angles change sunlit vs shaded fraction seen by the sensor
Clouds & aerosols
Contaminate large footprints; moderate broken clouds tolerated for Fraunhofer lines
Zero-level offset
Non-zero SIF retrieved where none exists (e.g. Sahara) — found first in GOSAT
Sensor performance
Spectral resolution, SNR, stray light, calibration drift and degradation
Notes: Even with a good algorithm, several effects can mimic or hide SIF. For O2 bands, the atmosphere must be modelled very accurately (path length, pressure, aerosols) either in two steps (TOA to TOC, then retrieval) or in one step. The direct-to-diffuse ratio changes band depth (up to ~20% error at O2-A). Canopy anisotropy and sun–sensor geometry change what fraction of sunlit and shaded leaves is seen. Satellites also suffer zero-level offsets, cloud and aerosol contamination and sensor degradation.

## Slide 55: Modelling SIF: from photosystem to globe
Mohammed et al. (2019), Fig. 5 — history of leaf and canopy models; blue = models without fluorescence
Photosystem
Kautsky, Genty, Rosema NPQ, van der Tol & Berry
Leaf RTM
PROSPECT → FluorMODleaf → Fluspect
Canopy 1D
SAIL → FluorSAIL → SCOPE (with energy balance)
Canopy 3D
DART, FluorFLIGHT, FluorWPS
Global LSM
CLM, BETHY, ORCHIDEE assimilate SIF
SCOPE = Soil–Canopy Observation of Photosynthesis and Energy fluxes; DART = Discrete Anisotropic Radiative Transfer
Notes: Models are essential to interpret SIF. Leaf physiological models describe how absorbed energy is partitioned (Genty equation, Rosema NPQ model, van der Tol & Berry). Leaf radiative transfer models describe absorption, emission and re-absorption inside the leaf (PROSPECT, FluorMODleaf, Fluspect). Canopy models add structure (FluorSAIL, SCOPE in 1D; DART, FluorFLIGHT, FluorWPS in 3D). Finally SIF is assimilated into global land surface models (CLM, BETHY, ORCHIDEE).

## Slide 56: 3D modelling example: DART simulation of a maize canopy
Mohammed et al. (2019), Fig. 6 — (a) irradiance, (b) sunlit (red) and shaded (blue) leaves, (c) true-colour reflectance, (d) PSII SIF image, (e) hourly PSII and PSI SIF at 742.5 nm
What 3D models add
Shadows, clumping, row structure, leaf angles — effects 1D models cannot represent.
SCOPE's niche
The only canopy model with leaf energy balance → links SIF, photosynthesis and temperature.
Uses
Interpret signals, design sensors, correct scattering/re-absorption, downscale SIF to photosystems.
Notes: DART represents every plant element in 3D, computes sunlit and shaded leaves through the day, and simulates reflectance and PSII/PSI fluorescence images. The hourly curve shows that canopy SIF follows the daily course of sunlight, with PSII and PSI contributions at 742.5 nm.

## Slide 57: Why SIF tracks photosynthesis (GPP)
GPP = APAR × LUE
SIF = APAR × ΦF × fesc
Shared term APAR (absorbed photosynthetically active radiation) explains much of the correlation. LUE = light-use efficiency; ΦF = fluorescence yield; fesc = escape probability.
What studies show
Strong far-red SIF–GPP correlation from tower to satellite
Mostly driven by APAR & chlorophyll
At constant APAR, SIF explained <35 % of GPP variability (Wohlfahrt 2018)
Shape of the relation
Hyperbolic on stress-free days, linear under stress
Becomes linear when aggregated over space/time
Differs for C₃ vs C₄ (e.g. Indo-Gangetic Plains)
Why NPQ matters
In high light NPQ diverts energy from both P and F
Midday depression of far-red SIF linked to NPQ
PRI (531 nm) helps track NPQ alongside SIF
Notes: Both GPP and SIF are proportional to absorbed PAR. GPP = APAR × light-use efficiency; SIF = APAR × fluorescence yield × escape probability. Much of the observed SIF–GPP correlation therefore comes from APAR (shared absorption by chlorophyll). The yield terms add physiological information, but their relationship is not fixed: it depends on NPQ, stress, structure and scale. Under stress-free days the relationship can be hyperbolic, under stress more linear; aggregation over space and time tends to linearise it.

## Slide 58: Measurement platforms: leaf to aircraft
Mohammed et al. (2019), Fig. 9 — trade-offs of hand-held, top-of-canopy and airborne instruments
Hand-held leaf
FluoWat clip + spectrometer; full spectrum; up- or downward SIF
Top-of-canopy
FloX, FluoSpec (0.13 nm), PhotoSpec, AutoSIF, NASA FUSION; diurnal & seasonal
UAV
AirSIF, HyUAS, Piccolo doppio; 30–40 cm pixels over tree crowns
Airborne
AIRFLEX, HyPlant (FLEX demonstrator), CFIS (OCO-2 validation)
Trade-off
Higher platforms → larger area and lower cost per area, but less physiological detail per pixel.
Notes: Each platform trades autonomy, cost and spatial coverage against physiological detail. Hand-held leaf devices (FluoWat leaf clip with short-pass filter) give the full SIF spectrum of single leaves. Top-of-canopy spectrometers on towers (FloX, FluoSpec, PhotoSpec, AutoSIF, FUSION) run automatically to capture diurnal and seasonal dynamics. UAVs give very high spatial resolution. Airborne imagers (AIRFLEX, HyPlant, CFIS) map fields and validate satellites.

## Slide 59: UAV and airborne SIF maps
Fig. 10 — UAV SIF (O₂-A, 3FLD) over an olive orchard (left) and water-stressed citrus (right)
Fig. 11 — HyPlant reflectance (top) vs F₇₆₀ SIF (bottom); fields A and B differ only in SIF
UAV strength
Very high spatial resolution, flexible on-demand flights; must stay light yet keep SNR.
Airborne strength
HyPlant: 0.25 nm resolution, 670–780 nm; maps both red and far-red SIF.
Notes: Left: a fixed-wing UAV with a micro-hyperspectral imager retrieved SIF (3FLD, O2-A) from 30–40 cm pixels over an olive orchard and a water-stressed citrus field, isolating pure tree crowns from shadow and soil. Right: HyPlant maps over Klein Altendorf, Germany. Fields A and B look almost identical in reflectance but have very different SIF, showing that fluorescence carries information not visible in reflectance.

## Slide 60: Satellites that measure SIF
Mission / sensor | Status (2019) | Footprint (km²) | Overpass | Repeat | Range (nm) | FWHM (nm) | SIF
FLEX / FLORIS | Selected | 0.3 × 0.3 | 10:00 | 27 day | 500–780 | 0.3–2.0 | Red, far-red, full, PRI
Sentinel-5P / TROPOMI | In orbit | 7 × 7 | 13:30 | 16 day† | 675–775 + | 0.5 | Far-red, full, (red)
MetOp / GOME-2 | In orbit | 40 × 40 / 40 × 80 | 09:30 | 29 day† | 270–790 | 0.5 | Far-red, full, (red)
OCO-2 | In orbit | 1.3 × 2.25 | 13:30 | 16 day | 757–775 | 0.04 | Far-red
GOSAT / TANSO-FTS | In orbit | 10 × 10 | 13:00 | 3 day | 758–775 + | 0.025 | Far-red
TanSat / ACGS | In orbit | 2 × 2 | 13:30 | 16 day | 758–778 + | 0.04 | Far-red
TEMPO · Sentinel-4 · GeoCARB | Selected (GEO) | ~3–8 km | GEO | hourly | various | 0.05–0.6 | Far-red (± red)
Simplified from Table 3 of Mohammed et al. (2019). †Daily near-global coverage thanks to wide swaths; repeat cycle refers to identical orbit tracks. '+' = additional bands at longer wavelengths.
Rule of thumb: high spectral resolution, high SNR, small footprint and frequent revisit cannot all be maximised at once.
Notes: None of the early satellites were designed for SIF; they were built for atmospheric chemistry (CO2, methane, ozone), but their high spectral resolution near the O2-A band allowed far-red SIF retrieval from Fraunhofer lines. FLEX will be the first mission designed specifically for SIF. Note the trade-offs: GOSAT and OCO-2 have very high spectral resolution but sparse sampling; GOME-2 large footprints; TROPOMI daily global coverage at 7 km.

## Slide 61: Global far-red SIF from space
Mohammed et al. (2019), Fig. 13 — 2009 annual average far-red SIF from GOME-2 (Joiner et al. 2013)
Reading the map
Red/yellow: highest SIF (tropics, intensive cropland)
Black: deserts, ice — no vegetation
Seasonal maps reveal phenology and drought
Satellite findings
GOME-2 SIF captured high US Corn Belt GPP that vegetation indices missed
Drought & heat stress signals at ecosystem scale
Notes: This annual 2009 map from GOME-2 shows where photosynthesis is most active: tropical forests, the US Corn Belt in summer, eastern China and northern India croplands. GOME-2 has about 0.5 nm resolution and SNR above 1000 near 740 nm, allowing monthly 0.5° maps. TROPOMI now gives daily data at 7 × 7 km, enough to see biome-scale patterns in much finer detail.

## Slide 62: FLEX: the first satellite designed for SIF
Mohammed et al. (2019), Fig. 12 — FLEX (FLORIS, 150 km swath) in tandem with Sentinel-3 (OLCI 1270 km; SLSTR nadir 1400 km, backward 740 km)
300 m
pixel size
500–780
nm spectral range
10:00
equatorial overpass
150 km
FLORIS swath
Planned products
Total fluorescence Ftot (650–780 nm); F685, F740; F687, F760
Photosynthetic activity, NPQ indicators (PRI), fAPARchl, LAI, chlorophyll
5-year mission, 56°S–75°N land and coastal zones
Notes: ESA's FLuorescence EXplorer, the 8th Earth Explorer, flies in tandem with Sentinel-3. Its single payload, FLORIS, is a dual imaging spectrometer covering 500–780 nm with high spectral resolution in the red and far-red, giving the full fluorescence spectrum, the red and far-red peaks, O2-B and O2-A features, and reflectance indices such as PRI. Sentinel-3's OLCI and SLSTR provide atmospheric, thermal and land-cover information. The review gave a projected launch of 2022; the launch has since moved later.

## Slide 63: What SIF is used for
GPP & carbon uptake
Empirical and model-based GPP from tower to globe
Phenology & seasons
Green-up, peak, senescence; seasonal dynamics
Drought & water stress
SIF ↓ with water deficit; pair with canopy–air temperature
Heat stress
Detected from satellite during heat waves
Nitrogen deficit
Red/far-red SIF ratio ↑ with N deficiency
Plant disease
Xylella in olive (>80 %), Verticillium, Phytophthora
Herbicide damage
Detected before visible symptoms; reflectance unchanged
Transpiration
Linked to stomatal behaviour in unstressed crops
Notes: Table 4 of the review lists applications. In photosynthesis: APAR, diurnal and seasonal dynamics, GPP (empirical and modelled), light-use efficiency, phenology, vegetation type. In stress detection: bacterial infection (Xylella fastidiosa in olive, detected with >80% accuracy combined with thermal and other indices), fungal infection, heat, herbicide, nitrogen deficit, transpiration and drought. SIF is often combined with ancillary indices like NDVI, PRI, MTCI and canopy-minus-air temperature.

## Slide 64: What drives SIF? (Table 5 of the review)
Table 5 (part 1): vegetation traits and processes
Table 5 (part 2): environmental, atmospheric and stress factors
Process: A absorption · R re-absorption · S scattering · PQ photochemical quenching · NPQ · OP other photoprotection Scale: L leaf · C canopy · E ecosystem · B biome Time: ST short · MT medium · LT long-term · SV seasonal
Notes: Every factor in this table can change SIF through one or more processes: absorption of incident light (A), re-absorption (R), scattering (S), photochemical quenching (PQ), NPQ, or other photoprotection (OP). The right-hand columns show at which ecological scale (leaf, canopy, ecosystem, biome) and timescale each matters. Use it as a checklist before interpreting a SIF change as 'photosynthesis changed'.

## Slide 65: Challenges and future directions
Disentangle drivers
Separate physiology from structure, pigments and illumination using models + ancillary data
Quantify NPQ
PRI, reflectance 500–600 nm, canopy–air temperature to constrain the SIF–photosynthesis link
Validate retrievals
Ground towers, UAVs and airborne demonstrators (HyPlant, CFIS) under satellite tracks
Scale bridging
Downscale coarse satellite SIF; correct directional effects; combine sensors
Better sensors
Red + far-red + full spectrum; high spectral resolution and SNR; VNIR for inversion
Operational products
Assimilation in land surface models; ML emulators; tools for non-experts
Notes: The review's main messages: understand confounding factors, validate satellite retrievals with ground and airborne data, quantify NPQ (with PRI or temperature differences), deliver user-friendly products, and combine spatial and temporal scales. Practical farming needs ~20 m spatial resolution and frequent revisits; forests need high spatial detail; high latitudes need very high SNR. Geostationary missions, FLEX and machine-learning emulators are expected to move SIF from research to operational use.

## Slide 66: Synthesis & self-check
Bringing PAM and SIF together, a one-page formula sheet, and answers to the most common doubts
09
Notes: Use these slides for revision.

## Slide 67: One concept, two ways of measuring it
Absorbed light energy
ΦP + ΦN + ΦF = 1
ACTIVE · PAM fluorometry
Controls light: ML, AL, saturating pulse, FR
Measures yields: Fv/Fm, ΦPSII, qP, qL, NPQ
Separates photochemical vs non-photochemical quenching
Leaf / plant scale; mechanistic understanding
PASSIVE · Sun-induced fluorescence
Sunlight as source; in-filling of O₂ bands / Fraunhofer lines
Measures flux: SIF = APAR × ΦF × fesc
Linked to GPP mainly via APAR; NPQ and structure confound
Canopy to global scale; ecosystem monitoring
Notes: Both approaches start from the same partitioning of absorbed energy into photochemistry, heat and fluorescence. PAM manipulates light to measure yields and separate photochemical from non-photochemical quenching. SIF measures the fluorescence flux under natural light, which combines how much light is absorbed with the yield and escape of fluorescence, and is related to GPP mainly through APAR.

## Slide 68: Formula sheet
Fv
Fm − Fo
Fv/Fm
(Fm − Fo)/Fm ≈ 0.83 healthy
Fq′
Fm′ − F′
Fv′
Fm′ − Fo′
ΦPSII
(Fm′ − F′)/Fm′ = qP × Fv′/Fm′
qP
(Fm′ − F′)/(Fm′ − Fo′)
qL
qP × Fo′/F′
NPQ
(Fm − Fm′)/Fm′
qN (old)
1 − (Fm′ − Fo′)/(Fm − Fo)
ETR
ΦPSII × PAR × 0.84 × 0.5
Fo′ (calc.)
Fo/[(Fv/Fm) + (Fo/Fm′)]
TOC radiance
L = r·E/π + SIF
FLD
F = (EoutLin − EinLout)/(Eout − Ein)
SIF / GPP
SIF = APAR·ΦF·fesc ; GPP = APAR·LUE
Prime (′) = light-adapted. No prime = dark-adapted. Green = PAM parameters; red = PAM extras and SIF.
Notes: All formulas in one place for revision.

## Slide 69: Clearing common doubts (1/2): PAM
Why does fluorescence rise when reaction centres close?
Photochemistry stops (kP ≈ 0), so the same excitation must leave by heat or fluorescence. Competition → fluorescence yield rises to Fm.
Why is Fm′ lower than Fm?
In the light NPQ is active. Even with all centres closed by the pulse, extra heat dissipation competes with fluorescence.
Why measure Fv/Fm in the dark but ΦPSII in the light?
Fv/Fm needs all centres open and NPQ = 0 (maximum potential). ΦPSII describes actual efficiency under the current light.
Does a drop in Fv/Fm mean lower photosynthesis?
Not necessarily: it reflects light-limited yield; light-saturated photosynthesis may be unchanged, and stress elsewhere may not show.
Notes: Questions students most often ask. Try answering each before reading the answer.

## Slide 70: Clearing common doubts (2/2): SIF
If fluorescence competes with photosynthesis, why does SIF correlate positively with GPP?
Both scale with absorbed light (APAR). Across space and seasons, APAR variation dominates; yield changes are smaller and partly co-vary.
Why is red SIF lower than far-red SIF?
Chlorophyll re-absorbs red light (absorption up to ~720 nm); far-red mostly escapes. PSI also adds far-red.
Why use absorption bands at all?
Outside the bands SIF is ~1–5 % of reflected radiance; inside O₂ bands sunlight is dim and in-filling by SIF can exceed 10 %.
Why can't satellites measure NPQ like PAM?
No saturating pulse can be applied from space. NPQ is approached indirectly, e.g. with PRI or temperature.
Notes: Questions students most often ask. Try answering each before reading the answer.

## Slide 71: Key references
Murchie E.H., Lawson T. (2013). Chlorophyll fluorescence analysis: a guide to good practice and understanding some new applications. J. Exp. Bot. 64(13): 3983–3998. doi:10.1093/jxb/ert208
Mohammed G.H. et al. (2019). Remote sensing of solar-induced chlorophyll fluorescence (SIF) in vegetation: 50 years of progress. Remote Sens. Environ. 231: 111177. doi:10.1016/j.rse.2019.04.030
Baker N.R. (2008). Chlorophyll fluorescence: a probe of photosynthesis in vivo. Annu. Rev. Plant Biol. 59: 89–113.
Maxwell K., Johnson G.N. (2000). Chlorophyll fluorescence — a practical guide. J. Exp. Bot. 51: 659–668.
Genty B., Briantais J.M., Baker N.R. (1989). Quantum yield of photosynthetic electron transport and quenching of chlorophyll fluorescence. BBA 990: 87–92.
Kramer D.M. et al. (2004). New fluorescence parameters for the determination of QA redox state. Photosynth. Res. 79: 209–218.
Oxborough K., Baker N.R. (1997). Resolving chlorophyll a fluorescence images… calculation of qP and Fv′/Fm′ without measuring Fo′. Photosynth. Res. 54: 135–142.
Strasser R.J. et al. (2004). Analysis of the chlorophyll a fluorescence transient. In: Advances in Photosynthesis and Respiration 19: 321–362.
Meroni M. et al. (2009). Remote sensing of solar-induced chlorophyll fluorescence: review of methods and applications. Remote Sens. Environ. 113: 2037–2051.
Drusch M. et al. (2017). The FLuorescence EXplorer mission concept — ESA's Earth Explorer 8. IEEE TGRS 55: 1273–1284.
Notes: Primary sources for this deck. The two review papers are the backbone; the others are classics cited within them for deeper reading.